# LIST CC UNN REM 112
 ,FONT 1 27 9
 ,PRINT 100
 ,END
1************************************************************
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *           ALP: Assembly Language Preprocessor            *
 *                                                          *
 *                       User's Guide                       *
 *                                                          *
 *                                                          *
 *                  Computer Center Branch                  *
 *       Division of Computer Research and Technology       *
 *              National Institutes of Health               *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 *                                                          *
 ************************************************************
 
 
                                      Version 6.19    5/10/88
1
1                    Level 2 Software Support
                      (Revised November 1986)
 
 This software product, or a  certain  portion  of  it,  has  been
 assigned Level 2 support status.  The Level 2 designation is made
 by the Computer Center for  any  of  three  reasons:   First,  an
 entire  software  product  may  be designated Level 2 if it is in
 test  status,  or  the  Center  determines  that  rapid   problem
 resolution  and long-term product availability can not be ensured
 with the vendor  support  available.   Second,  an  interface  to
 specific   peripheral   hardware   devices  (e.g.,  terminals  or
 plotters) will receive Level 2 support, even if the remainder  of
 the  product  is  designated  Level  1.   Third,  an interface to
 processors not at the NIH Computer Utility (e.g., microprocessors
 or  other  computer  installations) will receive Level 2 support,
 even if the remainder of the product is designated Level 1.
 
 If a hardware device/terminal is not  specifically  mentioned  in
 the  documentation  for  this  product,  no  interface  to  it is
 supported (even as  Level  2).   While  unsupported  devices  may
 sometimes  function  with  the  interfaces provided, any problems
 encountered are wholly the user's responsibility.   This  support
 policy  is  necessary  in order to provide services for the large
 number of devices (e.g.,  terminals,  plotters,  microprocessors)
 commonly  owned/used  by  end users.  It is not practical for the
 NIH  Computer  Center  to   be   familiar   with   the   hardware
 characteristics  of the myriad devices that can take advantage of
 these services.
 
 Users of this product should be fully aware that Level 2 software
 support  provides  documentation, non-critical Programmer Trouble
 Report (PTR) service, and limited  INTERFACE  preannouncement  of
 changes,   but  does  not  guarantee  continued  availability  or
 conversion assistance if this software  is  discontinued  by  the
 vendor or the Computer Center.
 
 In addition, no Programmer  Assistance  and  Liaison  (PAL)  Unit
 consulting  will  be available on questions pertaining to the use
 of or problems with software  receiving  Level  2  support.   The
 Computer  Center  will  accept  PTRs  for  problems  if  they are
 accompanied by all of the documentation necessary  for  diagnosis
 and   resolution.    When   the   Computer  Center  staff  member
 responsible for the problem area described in a PTR for a product
 receiving Level 2 support receives all pertinent documentation on
 the problem, the staff member will frequently act as a  technical
 guide with the burden of the work remaining with the user.
 
 Resolving or circumventing problems with software receiving Level
 2  support  may  require  resources  (e.g., hardware/terminals or
 source code) that are not available to the Computer Center staff.
 Since the Computer Center is often completely unfamiliar with the
 specific devices/terminals involved, the vendor may be  the  sole
 source  of  vital  information required for problem resolution or
 circumvention.  For this reason, the "Critical"  designation  for
 PTRs  is  not  applicable  and will be disregarded by the Center.
 Once a PTR and all supporting documentation is  received  by  the
 Computer  Center, the work to get a resolution is a mutual effort
 of the user, the Computer Center and the  author  or  vendor  for
 products  designated  to  receive  Level  2  support.   Since the
 Computer Center must rely  on  the  cooperation/interest  of  the
1vendor/developer  of a product, it is possible that some problems
 may never be resolved.
 
 The effects of this reduced  support  from  the  Computer  Center
 should be thoroughly considered before incorporating any software
 receiving Level 2 support into critical applications.  It must be
 stressed that the proper functioning or long-term availability of
 software receiving Level 2 support cannot be  guaranteed  by  the
 Computer Center.
 
 The following chart outlines Computer Center  services  available
 for  software receiving Level 2 support.  For further information
 on Levels of software and how to submit PTRs, see the appropriate
 section  of the Computer Center Users Guide.  If questions remain
 on this policy, contact the PAL Unit Consulting Desk of  the  NIH
 Computer Center.
 
 
 
 SERVICE                            LEVEL 2 SOFTWARE SUPPORT
 
 CONSULTING (PAL DESK)
   a) personal visit                        No
   b) telephone                             No
                                         (Users will have to rely
                                         on technical documentation
                                         provided by the Computer
                                         Center and their own
                                         resources)
 
 PROGRAMMER TROUBLE REPORT (PTR)            Yes
 
 "CRITICAL" PTR DESIGNATION                 No
 
 REFUNDS                                    Yes
 
 DOCUMENTATION                              Yes
 
 TRAINING                                   Resources
                                            permitting
 SOFTWARE MAINTENANCE
  a) Currency maintained with respect       Resources
     to new versions and facilities         permitting
  b) Formal change testing (Test Job        No
     Stream)
  c) Informal change testing                Yes
  d) Guarantee of orderly, fully            No
     documented conversion if product
     is discontinued
  e) Preannouncement in INTERFACE of        Resources
     all new facilities                     permitting
  f) Preannouncement in INTERFACE of        Resources
     changes which cause old versions       permitting
     of programs to function
     incorrectly or differently
  g) Preannouncement in INTERFACE of        Yes
     discontinuance of support or changes
     in support status (Level)
  h) Preventive and corrective fixing       Resources
     by Computer Center staff               permitting
1
                         Table of Contents
 
 
 
 
 
    I. Introduction . . . . . . . . . . . . . . . . . . . . . .  1
 
   II. The ALP Language . . . . . . . . . . . . . . . . . . . .  3
 
        Input format  . . . . . . . . . . . . . . . . . . . . .  3
        Comment convention  . . . . . . . . . . . . . . . . . .  3
        Statement differentiation . . . . . . . . . . . . . . .  4
        Compound statements . . . . . . . . . . . . . . . . . .  5
        Predicates  . . . . . . . . . . . . . . . . . . . . . .  6
 
  III. ALP Statements . . . . . . . . . . . . . . . . . . . . .  8
 
        Conditional and alternative statements  (IF). . . . . .  8
        Loop statements (DO). . . . . . . . . . . . . . . . . .  9
        Case selection  (CASE). . . . . . . . . . . . . . . . . 14
        Predicate selection (SELECT). . . . . . . . . . . . . . 16
        Loop control mechanisms (EXIT and NEXT) . . . . . . . . 18
        Branching (GOTO and RGOTO). . . . . . . . . . . . . . . 20
        Control of base register assignment (USE) . . . . . . . 21
        Inline data (DATA)  . . . . . . . . . . . . . . . . . . 22
        Conditional assembly  (ASM) . . . . . . . . . . . . . . 23
        Including ALP code in macros  (MACRO) . . . . . . . . . 26
        Reversion to BAL  (BAL) . . . . . . . . . . . . . . . . 28
        Block Comments (COMMENT). . . . . . . . . . . . . . . . 29
        Listing format control (TITLE,SUBTITLE,EJECT,SPACE) . . 30
 
   IV. Non-Control Extensions . . . . . . . . . . . . . . . . . 32
 
    V. The Implementation of ALP  . . . . . . . . . . . . . . . 34
 
   VI. ALP Syntax . . . . . . . . . . . . . . . . . . . . . . . 35
 
  VII. ALP Readability Macros . . . . . . . . . . . . . . . . . 39
 
 VIII. Macros for Environment Enhancement . . . . . . . . . . . 41
 
       AREA and AREAEND . . . . . . . . . . . . . . . . . . . . 42
       DEBLANK  . . . . . . . . . . . . . . . . . . . . . . . . 45
       EDIT . . . . . . . . . . . . . . . . . . . . . . . . . . 47
       EXI  . . . . . . . . . . . . . . . . . . . . . . . . . . 49
       MCLC, MMVC, MNC, MOC and MXC . . . . . . . . . . . . . . 51
       MFC  . . . . . . . . . . . . . . . . . . . . . . . . . . 52
       MTC  . . . . . . . . . . . . . . . . . . . . . . . . . . 53
       MTR  . . . . . . . . . . . . . . . . . . . . . . . . . . 54
       MTRT . . . . . . . . . . . . . . . . . . . . . . . . . . 55
       MZC  . . . . . . . . . . . . . . . . . . . . . . . . . . 56
       DF . . . . . . . . . . . . . . . . . . . . . . . . . . . 57
       SF . . . . . . . . . . . . . . . . . . . . . . . . . . . 58
       TF . . . . . . . . . . . . . . . . . . . . . . . . . . . 59
       ZF . . . . . . . . . . . . . . . . . . . . . . . . . . . 60
1
 
       OSCALL . . . . . . . . . . . . . . . . . . . . . . . . . 61
       OSENTER  . . . . . . . . . . . . . . . . . . . . . . . . 62
       OSEXIT . . . . . . . . . . . . . . . . . . . . . . . . . 63
       OSSETUP  . . . . . . . . . . . . . . . . . . . . . . . . 64
       OPENP  . . . . . . . . . . . . . . . . . . . . . . . . . 66
       CBDELINK . . . . . . . . . . . . . . . . . . . . . . . . 67
       CBDLINKH . . . . . . . . . . . . . . . . . . . . . . . . 69
       CBDLINKT . . . . . . . . . . . . . . . . . . . . . . . . 70
       CBLINK . . . . . . . . . . . . . . . . . . . . . . . . . 72
       CBLINKH  . . . . . . . . . . . . . . . . . . . . . . . . 73
       CBLINKT  . . . . . . . . . . . . . . . . . . . . . . . . 74
 
   IX. ALP Coding Hints . . . . . . . . . . . . . . . . . . . . 75
 
    X. Sample Program . . . . . . . . . . . . . . . . . . . . . 76
 
   XI. Using ALP at NIH . . . . . . . . . . . . . . . . . . . . 80
 
  XII. References . . . . . . . . . . . . . . . . . . . . . . . 82
1                           - 1 -
 
 
                       I. INTRODUCTION
 
      The choice of the proper vehicle  --  assembly  language  or
 higher-level language -- for writing so-called "systems programs"
 is  a  subject  of  constant  debate  (1,2).   With a few notable
 exceptions (3,4), the trend has  been  toward  continued  use  of
 assembly  languages,  generally  those  provided  by  vendors  of
 computer  systems.   Fortunately,  the  field  is now well enough
 explored  that   most   assemblers   are   relatively   powerful,
 incorporating  macro  or preprocessor facilities such as symbolic
 substitution, conditional assembly, etc.  Given the  architecture
 of  most  currently-available  hardware  and  the  orientation of
 assemblers toward that hardware, very little  has  been  done  to
 provide  sophisticated  control  or data structures.  Considering
 that until fairly recently  this  was  also  the  case  even  for
 compiler-level languages, perhaps it is not too surprising.
 
      For better  or  worse,  systems  being  implemented  at  the
 assembly  language  level have -- inevitably -- grown in size and
 complexity.  This is one of the major  factors  (along  with  the
 desire  to  work in terms closer to the nature of the application
 being developed)  that  led  to  the  evolution  of  higher-level
 languages.   It  has  also  fostered  the  investigation  of more
 powerful tools  for  building  systems  whose  implementation  is
 constrained,  for  one  reason or another, to the use of assembly
 language.   The  various  approaches  taken  have  included  more
 powerful macro facilities, compilers for languages which  can  be
 straightforwardly  and  efficiently  translated (some into object
 code, others into assembly  source),  highly-optimized  compilers
 which  attempt to relieve the concerns about staying close to the
 underlying hardware, and preprocessors which provide capabilities
 similar to those available with macro systems but with  increased
 flexibility.   It  is  a  tool  of  this  last type which will be
 described below.
 
     Our  search  for  a  means  of   making   assembly   language
 programming easier began in the first place because we were faced
 with  a  large project which we had already decided would be done
 in assembly language.  This was due to the environment  in  which
 the  end result would operate, efficiency considerations, and the
 lack of any reasonable alternative, as well  as  experience  with
 previous  versions  of  the system.  It was obvious, though, that
 features not provided by the available assemblers  would  greatly
 improve  both  the speed with which the project could proceed and
 its eventual maintenance and  enhancement.   The  most  realistic
 goal  was  to provide better control structures, perhaps assembly
 language's most serious deficiency.  In addition,  we  sought  to
 improve  the  overall reliability of the new system by minimizing
 the chances of certain types of coding and logic errors which are
 encouraged by the scarcity of good  control  structures  and  the
 consequent  requirement  for  explicit  branching,  labels,  etc.
 Hence  some  form of "structured" programming technique seemed to
 be indicated.
1                           - 2 -
 
 
      For reasons of practicality, we preferred to  use  something
 already developed and in use.  A preprocessor (AL) which provided
 many  of  the  features we were looking for had been developed by
 Edward C.  Haines at MITRE, and we decided to use that as a  base
 (portions of this document are taken from the original  reference
 (5)).  The salient features of AL were that it provided:
 
      . "predicates" for condition testing
      . an "IF ... THEN ... ELSE ..." structure
      . "WHILE ... DO ..." and "DO ... UNTIL ..."
      . a "COUNT" statement for iterative loops
      . a conditional branching capability
 
      in addition, it allowed:
 
      . free-form input, with label and statement delimiters
      . comments
      . transparent use of regular assembly language
 
      After acquiring the source for AL and examining it, we  made
 a number of enhancements.  These include:
 
      . extension of predicates to allow grouping
      . generalization of the loop control structures into
        .. DO-WHILE   / WHILE-DO
        .. DO-UNTIL   / UNTIL-DO
        .. DO-FOR     / FOR-DO  (replacing AL's "COUNT")
        .. DO-FOREVER / FOREVER-DO (replacing AL's "LOOP")
      . addition of CASE and SELECT statements
      . generalization of explicit branching to allow
        .. GOTO (replacing AL's "BIF")
        .. RGOTO (for register form of branch)
      . improved loop controls
        .. EXIT
        .. NEXT
      . local control  of  base  register  assignment  for  DSECTs
        through USE
      . access to  conditional  assembly  facilities  through  the
        ASM statements
      . support for ALP code in macros through the MACRO statement
      . substitution of '<'/'>' and 'BEGIN'/'END' for AL's use  of
        parentheses as compound statement delimiters
      . recording of nesting level and display on listing
      . automatic indentation according to nesting level
      . provision for title and subtitle control as well as  eject
        and space
      . allowance for presence of  macro  variables  (i.e.   those
        beginning with "&") in operand fields
      . acceptance of macro and sequence symbols as labels
      . limited optimization of internally-generated branches
 
      Fortunately,  AL  proved  to  be  a  reasonable  basis   for
 expansion.   Our  task  would  have  been far greater had we been
 forced to start from scratch.
1                           - 3 -
 
 
                     II. THE ALP LANGUAGE
 
      Following sections will describe each ALP statement in  some
 detail.  A syntax description in augmented BNF  is  contained  in
 section VI.
 
 
 INPUT FORMAT
+____________
 
      ALP resembles PL/I in some respects.  Programs are  composed
 of  statements,  separated by semi-colons (';').  Source code may
 be entered in free form in columns  1-72  (columns  73-80  should
 contain  some sort of sequence information).  The program must be
 terminated with an "END" statement (i.e.   "END;").   Labels  are
 delimited  by  a colon (':'), and multiple labels may appear on a
 single statement.  Otherwise, labels obey assembler  conventions.
 That  is, they must be one to eight characters in length, consist
 of 'A'-'Z', '0'-'9', '$', '@', or '#', and  begin  with  'A'-'Z',
 '$', '@', or '#'.
 
      In order to allow for sequence  symbols,  set  symbols,  and
 labels  into  which  macro  variables are to be substituted, '.',
 '&', '(', and ')' are also allowed.  Ampersands should be doubled
 in order to prevent confusion with the AND operator.
 
 Examples:
 
  program:
 
      S1; S2; S3; END;
 
  labeling:
 
      LABEL: S;
      L1: L2: S;
      .SEQ: AGO .SEQ2;
      &&CHAR: SETC 'ABC';
      X&&Y(2)Z: DC H'0';
 
 
 COMMENT CONVENTION
+__________________
 
      Like PL/I, ALP allows comments wherever a  blank  is  legal.
 However,  the  delimiting  mechanism  is  quite  different.   ALP
 comments  begin  with  a percent sign ('%') and are terminated by
 the end of the input line.
 
 
 Examples:
 
           LA  R1,2;  % THIS IS A COMMENT
 
 Block comments are also supported, see section III.
1                           - 4 -
 
 
 STATEMENT DIFFERENTIATION
+_________________________
 
      There are two types of ALP statements, which, unless  stated
 otherwise  will  be  treated  equivalently  in  the  rest of this
 document.  The  first  type  consists  of  those  beginning  with
 keywords  meaningful  to  ALP,  which  it  processes.  The second
 consists of those which ALP does not recognize and passes  on  to
 the  assembler  on the assumption that they are BAL statements or
 macro calls.
 
      In the latter type, the usual  assembler  conventions  about
 operand fields apply, with three changes:
 
   1. Comments must be entered  as  described  above  --  a  blank
      signals only the end of the field, not the start of comments
      as well.
 
   2. If an ampersand ('&') is to appear in an operand other  than
      inside a quoted string, it must be doubled to distinguish it
      from  ALP's predicate conjunction operator (see below).  For
      example:
 
           LA REG,&&CON;
           LA REG,=C'&STRING';
 
   3. Since ALP  input  is  free  form,  the  only  place  special
      continuation  is  required  is  when  operand fields must be
      split across line boundaries.  In such cases, end the  first
      part of the field with an underscore -- it will be continued
      with  the next non-blank character (ignoring any intervening
      comments) and the underscore will be discarded.  If a quoted
      string  must  be  broken,  end  the  first   part   with   a
      quote-underscore  pair and continue with a quote on the next
      line.  The underscore, any intervening blanks, and  the  two
      extra quotes will be discarded.  For example:
 
           TPUT MESSAGE,_
                LENGTH;
 
      and
 
           DC C'THIS IS A LONG CONSTANT '_
               'WHICH WILL BE CONTINUED';
1                           - 5 -
 
 
 COMPOUND STATEMENTS
+___________________
 
      Simple statements may be combined into  compound  statements
 by   enclosing   them   in   angle  brackets  ("<"  and  ">")  or
 "BEGIN"-"END" symbols and separating them with semicolons.
 
 
 Examples:
 
      <S1; S2; S3>
 
      BEGIN
         S1;
         S2;
         S3;
         END
 
 
 Spacing is irrelevant, except that  there  must  be  a  delimiter
 (such  as a blank) following the "BEGIN" and preceding the "END".
 Also, there is no semicolon required preceding the "END" or  ">".
 However,  a  semicolon  must follow a compound statement wherever
 one is required after a simple statement.
 
      Although "BEGIN"-"END"  and  "<"-">"  are  generally  inter-
 changeable, special consideration must be taken in two cases:
 
 1) An  "END"  bracket  must  never  be  labeled.   An  acceptable
    equivalent  is  a  labeled  null   statement   preceding   the
    terminating bracket.  For example:
 
      BEGIN
         statement;
         statement;
         label: ;
         END
 
 2) If the  final  statement  in  a  group  of  statements  to  be
    bracketed  has  no  operands,  a  semicolon  must  precede the
    terminating "END" or the "<"/">" form must be used to  prevent
    the "END" from being mistaken for an operand on the statement.
1                           - 6 -
 
 PREDICATES
+__________
 
      The concept necessary for most control structures  is   that
 of  predicate.   A  predicate  is  a  sequence of statements that
 produces a truth value.  On  the  System/370,  testing  of  truth
 conditions  is accomplished  by  setting  a  condition code (with
 an instruction such as  a  comparison)  and  then   conditionally
 branching   on   the  status   of   the   condition   code.   The
 instructions that set the condition code are sometimes,  but  not
 often,   what   people   logically  want   to  think  of  as  the
 predicate.   The  execution  of  conditional  branches  is almost
 always not what people want  to  think  about  (cf Dijkstra(6)).
 
     In ALP, a simple predicate  is  a  sequence  of  instructions
 (possibly  empty)  that  defines  a  condition  code  setting.  A
 predicate is then a  Boolean  combination  of  simple  predicates
 involving the operators '&' ("AND"), '|' ("OR"), and '^' ("NOT").
 The   conditional  branches  (and  unconditional  branches  where
 necessary) are implied by the control statements.  The programmer
 is, for the most part, freed from worrying about  what  condition
 code value(s) will be set and how to test them.
 
 *****************************************************************
      A number  of  macros  have  been  provided  to  improve  the
 readability of ALP programs and to provide additional information
 for  ALP's use in determining condition tests, etc.  They will be
 used freely in the examples that follow:  see sections  VII   and
 VIII for complete information.   Note that use of these macros is
 not required.
 *****************************************************************
 
 Examples:
 
  simple predicate:
 
      <CLI  BUFFER,C'*'>
 
      <L R15,RETCODE; RZ R15>
 
  predicate:
 
      ^<CLI BUFFER,C' '>
 
      <CLC WORD,=C'ERROR'> & <RNP R15> | <TM EBITS,X'80'>
 
      <<CLC WORD,=C'ERROR'> & <RNP R15>> | <TM EBITS,X'80'>
 
      Grouping is such that a&b|c&d is interpreted as a&(b|(c&d));
 there is no operator precedence, but grouping  of  predicates  in
 angle  brackets  is  allowed.   IF,  DO, etc.  should not be used
 within a predicate because  they  introduce  uncertainty  in  the
 condition actually being tested.  The way in which predicates are
 evaluated  does  not  always  insure that all instructions in the
 predicate  are  executed.   Thus,  care  should  be  taken   that
 processing  does  not depend on the execution of all instructions
 in  a  predicate  involving  Boolean   combinations   of   simple
 predicates.
1                           - 7 -
 
 
      The appropriate condition code test is determined  from  the
 op-code  of  the  last statement of the predicate; if the name is
 not recognized, the default is '=' (equal, or  zero).   The  test
 can  be  explicitly specified by using a special statement of the
 form:
 
      CC ccstring
 
 where ccstring is composed of characters from the set
 
      0 = E Z   1 L M   2 P H   3 O   N ^
 
      These are used as in the form of the extended  mnemonics  of
 the  assembler except that they specify the "truth" condition (as
 opposed  to  the  branch  condition)  and  any   combination   of
 characters is allowed.
 
      Since equality is the appropriate truth condition  for  most
 predicates,   only   non-standard   cases   are  coded  into  the
 preprocessor.  These are:  OPENP (NZ), TF (NZ), TM (NZ), TS (NZ),
 TRT (NZ), RM (M), RZ (Z), RP (P), RMZ (NP), RMP (NZ),  RZP  (NM),
 RNM (NM), RNZ (NZ), RNP (NP), RNMZ (P), RNMP (Z), RNZP (M).
1                           - 8 -
 
 
                     III. ALP STATEMENTS
 
 
 CONDITIONAL AND ALTERNATIVE STATEMENTS
+______________________________________
 
     Conditional and alternative statements are  provided  by  the
 IF-THEN-ELSE statement.  Its format is:
 
     IF predicate THEN statement ELSE statement
 
 where the "ELSE" clause is optional.
 
 
 Examples:
 
     IF <LH R2,0(R1); RP R2> THEN STH R2,BLKSIZE;
 
 at assembly time would appear (subject to label differences) as:
 
        LH  R2,0(R1)
        LTR R2,R2
        BNP @0001
        STH R2,BLKSIZE
  @0001 ----
 
 
     IF  <L R2,0(,R3); RZ R2>
     THEN LA R3,1
     ELSE LA R3,2;
 
 would generate:
 
        L   R2,0(R3)
        LTR R2,R2
        BNZ @0001
        LA  R3,1
        B   @0002
  @0001 LA  R3,2
  @0002 ----
 
 
 NOTE:  If  a  simple  statement  without  operands  (such  as  an
 operand-less   machine  op-code  or  macro  call)  comprises  the
 predicate or the "THEN" clause in an "IF  ...   THEN  ...   ELSE"
 construct,  it  must be enclosed in '<'/'>' bracketing symbols to
 prevent the following  keyword  ('THEN'  or  'ELSE')  from  being
 interpreted as an operand of the statement.
 
 *****************************************************************
 Note that ALP-generated labels begin with a commercial  "at-sign"
 ('@').   Labels  generated outside macro definitions will consist
 of an at-sign followed by  a  four-digit  decimal  integer  (e.g.
 @0001).   Labels  generated inside a macro (see the discussion of
 support for ALP code in macros) will involve a special symbol  so
 that   multiple  invocations  of  the  macro  will  not  generate
 duplicate labels (e.g.  @&@001).
 *****************************************************************
1                           - 9 -
 
 
 LOOP STATEMENTS
+_______________
 
      There are four sets of loop-producing statements:
 
      . DO-WHILE   and  WHILE-DO
      . DO-UNTIL   and  UNTIL-DO
      . DO-FOR     and  FOR-DO
      . DO-FOREVER and  FOREVER-DO
 
      The two forms differ in  the  position  of  the  test  which
 terminates  the  loop:   whether  it comes after (as in the first
 form) or before (as in the second) the body  of  the  loop.   The
 format of the first set is:
 
     WHILE predicate DO statement
 
            or
 
     DO statement WHILE predicate
 
 
 
 Examples:
 
     WHILE ^<CR R3,R11> DO <MVI 0(R3),C' '; AI R3,1>;
 
 generates:
 
  @0001   CR   R3,11
          BE   @0002
          MVI  0(R3),C' '
          LA   R3,1(,R3)
          B    @0001
  @0002   ----
 
 
 
     DO <MVI 0(R3),C' '; AI R3,1> WHILE ^<CR R3,R11>;
 
 generates:
 
  @0001   MVI  0(R3),C' '
          LA   R3,1(,R3)
          CR   R3,R11
          BNE  @0001
1                           - 10 -
 
 
      The DO-UNTIL set is similar to the DO-WHILE set except  that
 the "sign" of the test is reversed.  Its format is:
 
     DO statement UNTIL predicate
 
            or
 
     UNTIL predicate DO statement
 
 
 
 Examples:
 
     DO <LR R1,R2; L R2,0(,R1); LA R2,0(,R2)>
     UNTIL <C ADR,EADR(R2); CC H>;
 
 translates to:
 
  @0001   LR   R1,R2
          L    R2,0(,R1)
          LA   R2,0(,R2)
          C    ADR,EADR(R2)
          BNH  @0001
  @0002   ----
 
 
 
     UNTIL <C ADR,EADR(R2); CC H>
     DO <LR R1,R2; L R2,0(,R1); LA R2,0(,R2)>;
 
 generates:
 
  @0001   C    ADR,EADR(R2)
          BH   @0002
          LR   R1,R2
          L    R2,0(,R1)
          LA   R2,0(,R2)
          B    @0001
  @0002   ----
1                           - 11 -
 
 
      A simple loop counting mechanism is provided by  the  DO-FOR
 set.   The  number  of  times  the  loop  is  to  be  executed is
 determined by the  value  of  a  specified  register  (set  by  a
 previous  statement)  on  entry  to  the  loop.   The register is
 decremented once per cycle until it is zero.  The format is:
 
     DO statement FOR register
 
            or
 
     FOR register DO statement
 
 
 
 Examples:
 
      DO <IC R1,0(R11); BAL R9,PCHAR; AI R11,1> FOR R12;
 
 translates to:
 
  @0001   IC   R1,0(R11)
          BAL  R9,PCHAR
          LA   R11,1(,R11)
          BCT  R12,@0001
 
 
 
      FOR R12 DO <IC R1,0(R11) ; BAL R9,PCHAR; AI R11,1>;
 
 generates:
 
          LTR  R12,R12
          BNP  @0002
  @0001   IC   R1,0(R11)
          BAL  R9,PCHAR
          LA   R11,1(,R11)
          BCT  R12,@0001
  @0002   ----
1                           - 12 -
 
 
      The last  of  the  loop  control  structures  are  also  the
 simplest:   a  "do-once"  structure  and  an  infinite loop, with
 responsibility for escaping from it placed on the programmer.
 
 The format of the "do-once" is:
 
      DO statement
 
      This form is useful where the statement is  a  compound  one
 containing  EXIT statements (described in a later section), which
 permit escape from the compound  statement.   Similarly,  a  NEXT
 statement (see below) occurring in such a compound statement will
 cause control to be transfered to the start of the statement.
 
 
 The format of the infinite loop is:
 
      DO statement FOREVER
 
             or
 
      FOREVER DO statement
 
 
 
 Examples:
 
      DO <AI  R2,1> FOREVER;
 
              and
 
      FOREVER DO <AI  R2,1>
 
 both translate to:
 
  @0001  LA  R2,1(,R2)
         B   @0001
1                           - 13 -
 
 
      The WHILE-DO/DO-WHILE, UNTIL-DO/DO-UNTIL, and  FOR-DO/DO-FOR
 constructs,  as  well as the "do-once" form, may also be followed
 by an optional "THEN statement".  This allows  the  specification
 of  action to be taken if and only if control "falls through" the
 DO (e.g.  when the  register  specified  in  a  FOR-DO  construct
 becomes zero), but not if  control  is  transfered  via  an  EXIT
 statement.  FOREVER-DO/DO-FOREVER cannot take a THEN clause.
 
 Example:
 
      DO BEGIN
         ...
         EXIT;
         ...
         END
      THEN BEGIN
         ...
         END;
 
 
 NOTE:  Introduction of THEN as part of the DO construct  requires
 care  in  the  nesting of statements under certain circumstances.
 Nesting of DO's within DO's can cause confusion of THEN's in  the
 same  way that nesting of IF's can cause confusion of ELSE's.  In
 either case bracketing symbols must be used to prevent  attaching
 the dependent clause to the inner statement instead of the outer.
1                           - 14 -
 
 
 CASE SELECTION
+______________
 
      The CASE  statement  permits  the  selection  of  an  action
 designated by the value of a register.  Its format is:
 
      CASE register MAX expression  MIN expression;
         case-label: statement;
         ...
         ENDCASE
 
      The case to be executed is designated by the contents of the
 specified register.  This  index  must  be  a  multiple  of  four
 greater  than  or  equal  to  zero and be contained in a register
 other than register zero.  A maximum value (used  to  generate  a
 branch table, but not checked at execution time) is required, and
 may  be  any  valid previously defined assembler expression which
 evaluates to a multiple of four greater than the  minimum  value.
 A  minimum  value  (also  used  to  generate the branch table) is
 optional, has a  default  value  of  0,  and  may  be  any  valid
 previously defined assembler expression.  The case to be executed
 is  designated  by  the value of the "case-label" assigned to it.
 Each  such  label  consists  of  an  assembler  expression,   two
 expressions separated by the keyword "THRU", or a series of these
 two types separated by commas.  As shown above, the case label is
 separated  from  the statement making up the case by a colon.  If
 duplicate or overlapping case labels are specified, the last  one
 takes  precedence.   This  allows  a default action to be defined
 which will take effect  if  a  case  is  specified  for  which  a
 statement was not otherwise provided.  If a default action is not
 provided,  a program check (invalid op-code) will occur if a case
 is specified for which no statement was entered.
 
 Example:
 
      CASE R15 MAX 16;
         0: ;
         4,16: LA R15,4;
         8 THRU 12: LA R15,8;
         ENDCASE;
 
 translates to:
 
         B   @0001(R15)
  @0001  B   @0002
         B   @0003
         B   @0004
         B   @0004
         B   @0003
  @0003  LA  R15,4
         B   @0002
  @0004  LA  R15,8
  @0002  ----
 
1                           - 15 -
 
 
      The CHECK option may be used in a CASE statement to  specify
 that  the  minimum and maximum values are to be checked.  An ELSE
 clause may be added after the ENDCASE to specify the action to be
 taken for an out of bounds value.  If no ELSE clause is used,  an
 operation exception will occur for an invalid value.
 
 Example:
 
      CASE R15 MAX 16 MIN 4 CHECK;
         4,16: LA R15,4;
         8 THRU 12: LA R15,8;
         ENDCASE
      ELSE ABEND 1234,DUMP;
 
 translates to:
 
         C   R15,=A(4)
         BL  @0004
         C   R15,=A(16)
         BH  @0004
         B   @0001-4(R15)
  @0001  B   @0002
         B   @0003
         B   @0003
         B   @0002
  @0002  LA  R15,4
         B   @0005
  @0003  LA  R15,8
         B   @0005
  @0004  ABEND 1234,DUMP
  @0005  ----
 
      The CASE  statement  may  also  have  a  THEN  clause  which
 functions in the same manner as for the DO statement.   The  THEN
 clause must follow an ELSE clause, if present.
1                           - 16 -
 
 PREDICATE SELECTION
+___________________
 
      The SELECT statement is analogous to the CASE  statement  in
 that  it  allows  the  selection  of  an action designated by the
 validity of a specified condition.  In the  CASE  statement  this
 condition  is  the  equality of the specified register to a value
 given in the "case-label".  In the SELECT statement the condition
 is the truth of one or more predicates which take  the  place  of
 CASE "case-label"s.  The format is:
 
      SELECT;
         predicate: statement;
         ...
         ENDSEL
 
      Execution of the statement is as follows: each predicate  is
 evaluated in turn and,  if  true,  its  associated  statement  is
 executed.   The  sequential nature of this process means that the
 execution of a selected statement can influence the  truth  of  a
 predicate  forming the selection-label on a later statement.  For
 example:
 
      LI R1,1;
      SELECT;
         <C R1,=F'1'>: <LI R1,2>;
         <C R1,=F'2'>: <LI R1,3>;
         ENDSEL;
 
 
 As in the previous example, multiple elements  of  the  selection
 list  may  be  executed  in  turn.   The SELECT FIRST form of the
 construct specifies that  only  the  first  statement  for  whose
 predicate  is  true will be executed, and no others "below" it --
 regardless of the fact that their predicates may  also  be  true.
 Applying this option to the example above:
 
      LI R1,1;
      SELECT FIRST;
         <C R1,=F'1'>: <LI R1,2>;
         <C R1,=F'2'>: <LI R1,3>;
         ENDSEL;
 
 In this case, only the first selected case ("LI R1,2")  would  be
 executed, since no other predicates would be tested.
1                           - 17 -
 
      An additional option, applicable to SELECT FIRST form  only,
 allows specification of an action to be performed if no predicate
 in the selection-list is true.  Its form is as follows:
 
      SELECT FIRST;
         predicate: statement;
         ...
         ENDSEL
      ELSE statement
 
 Example:
 
      LI R1,0;
      SELECT FIRST;
         <C R1,=F'1'>: <LI R1,2>;
         <C R1,=F'2'>: <LI R1,3>;
         ENDSEL
      ELSE LI  R1,4;
 
      A THEN clause may also be appended to  a  SELECT  statement.
 The  statement  following  THEN  is  executed  if  control "falls
 through" to the end of the statement but not if an EXIT statement
 is used.  For example;
 
      SELECT FIRST;
         <C R1,=F'1'>: <LI R1,2>;
         <C R1,=F'2'>: <LI R1,3>;
         ENDSEL
      ELSE LI R1,4
      THEN MH R1,=H'10000';
 
 NOTE:  Although the effect of  the  SELECT  FIRST  ...   ELSE  is
 easily  obtained  with  IF-THEN-ELSEs,  the  SELECT  construct is
 generally more readable, and may  clarify  the  processing  being
 carried out.
1                           - 18 -
 
 LOOP CONTROL MECHANISMS
+_______________________
 
      In  order  to  reduce  the  necessity  for  coding  explicit
 branches, ALP provides ways to escape from and reenter a  control
 structure.  The first is the EXIT statement, whose complete  form
 is:
 
      EXIT FROM label IF predicate
 
 where the "FROM label" and "IF predicate" clauses are optional.
 
 Examples:
 
      EXIT;
      EXIT FROM BLOCK1;
      EXIT IF <RP 15>;
      EXIT FROM BLOCK1 IF <RP 15>;
 
 NOTE: If both are specified, the FROM clause must precede the  IF
 clause.
 
      When used inside a loop  construct  (DO-WHILE,  etc.),  EXIT
 causes   control  to  be  transfered  to  the  first  instruction
 following  the  loop  (bypassing  any  THEN  clause).   The  EXIT
 statement may also be used inside a CASE or SELECT  statement  to
 terminate execution of the case.
 
      An EXIT without a FROM clause causes a transfer  of  control
 to  the  first  instruction  immediately  following the construct
 containing the EXIT.  An EXIT followed by a FROM clause causes  a
 transfer  of  control  to  the  first  instruction  following the
 construct whose label is specified  in  the  FROM  clause.   Both
 forms   may  be  modified  by  the  IF  clause  to  provide  both
 conditional and unconditional EXITs.
 
 Examples:  (target labels are shown only for reference)
 
      BLOCK1: DO BEGIN
         ...
         BLOCK2: DO BEGIN
            ...
            EXIT; % TO TARGET1
            ...
            EXIT FROM BLOCK1; % TO TARGET2
            ...
            END;
         TARGET1: ...
         ...
         END;
      TARGET2: ...
 
 
      FOREVER DO BEGIN
         LA R2,1(,R2);
         EXIT IF <CR R2,R3>;
         MVI 0(R2),C'*';
         END;
1                           - 19 -
 
      In an analogous manner, the NEXT statement,
 
      NEXT OF label IF predicate
 
 causes transfer of control, conditionally or unconditionally,  to
 the  point  at which the next iteration of the construct named by
 "label" begins (e.g.  to the "BCT" in a "FOR" structure).  If  no
 OF  clause is specified, the next iteration of the innermost loop
 is begun.  In a  CASE  or  SELECT  statement,  a  NEXT  causes  a
 transfer of control back to the point of case selection.
 
 
 
 Examples:
 
      WHILE <L R2,0(,R2); CR R2,R3; CC NE>
      DO <NEXT IF RZ R5; AI R4,1>;
 
      CASE R15 MAX 8;
         0: ;
         4: <NEXT IF LTR R3,R3; CALL ERROR>;
         8: CALL ERROR2;
         ENDCASE;
 
      SELECT;
         <C R2,=F'1'>: <LI R2,2; NEXT>;
         <C R2,=F'2'>: <AI R2,1>;
         ENDSEL;
 
      BLOCK1: DO BEGIN
         BLOCK2: DO BEGIN
            ...
            NEXT; % NEXT ITERATION OF BLOCK2
            ...
            NEXT OF BLOCK1; % NEXT ITERATION OF BLOCK1
            ...
            END WHILE <CR R2,R3>;
         END WHILE <RP R1>;
 
 
 
 NOTE:  If an EXIT or NEXT statement occurs in the THEN clause of
 a DO, CASE or SELECT statement, it applies to the containing
 statement.
 
 NOTE:  It is possible to code statements like:
 
      IF predicate THEN EXIT;
 
 However, this causes less efficient code to be generated than  if
 the EXIT statement had been used in the form
 
      EXIT IF predicate;
 
 Hence the latter form is recommended.  This is equally  true  for
 the NEXT statement.
1                           - 20 -
 
 BRANCHING
+_________
 
     The final control statement, an admission of our  failure  to
 write completely structured programs, is an explicit branch.  Its
 format is:
 
     GOTO label IF predicate
 
 A branch-register form is also available:
 
     RGOTO register IF predicate
 
 where the "IF" clauses in both forms are optional.
 
 
 
 Examples:
 
      GOTO  X;
 
 translates to:
 
      B  X
 
 
 
      RGOTO  REG;
 
 generates:
 
      BR  REG
 
 
 
      GOTO X2 IF <TM 0(R1),X'40'>;
 
 generates:
 
      TM  0(R1),X'40'
      BNZ X2
 
 
 
      RGOTO REG2 IF <SI R3,1; RZ R3>;
 
 generates:
 
      BCTR R3,0
      LTR  R3,R3
      BZR  REG2
 
 
 
 NOTE:  "GOTO/RGOTO ...  IF ..."  generates  more  efficient  code
 than  "IF  ...  THEN GOTO/RGOTO ...", and is therefore preferable
 (even though the latter may be easier to think of).
1                           - 21 -
 
 
 CONTROL OF BASE REGISTER ASSIGNMENT FOR DSECTS
+______________________________________________
 
      Control of base register assignment for DSECTs through USING
 and DROP assembler statements, while not difficult, is frequently
 not easy to relate to the processing being performed.  ALP's  USE
 statement  allows  explicit  use  of  a  data  structure  for the
 duration of a single statement  --  simple  or  compound  --  and
 automatically provides the appropriate USING and DROP directives.
 Its format is:
 
      USE register AS dsect-name IN statement
 
 
 
 Example:
 
      USE R12 AS MSGBLK IN L R11,MSGLEN;
 
 translates to:
 
      USING MSGBLK,R12
      L     R11,MSGLEN
      DROP  R12
 
 
 
      Multiple "register AS dsect-name" units  may  be  specified,
 using commas as separators.
 
 
 
 Example:
 
      USE R1 AS PARMBLK1, R2 AS PARMBLK2 IN BEGIN
         L  R3,PARM1;
         L  R4,PARM2
         END;
 
 generates:
 
      USING PARMBLK1,R1
      USING PARMBLK2,R2
      L     R3,PARM1
      L     R4,PARM2
      DROP  R1,R2
1                           - 22 -
 
 INLINE DATA
+___________
 
      The DATA statement may be used to branch around data  values
 which  are included with executable code for purposes of clarity.
 The general form is
 
      DATA statement
 
 Examples:
 
      DATA CON: DC F'99'
 
 translates to
 
         B   @0001
 CON     DC  F'99'
 @0001   ...
 
 
       DATA BEGIN
          CONS:
          DC F'99';
          DC F'999';
          END
 
 translates to
 
         B   @0001
 CONS    DC  F'99'
         DC  F'999'
 @0001   ...
1                           - 23 -
 
 
 CONDITIONAL ASSEMBLY
+____________________
 
      While it is, of course,  possible  to  use  the  assembler's
 conditional  assembly  facilities in a straightforward way, it is
 often more convenient to have ALP generate the necessary sequence
 symbols, take  care  of  isolation  of  labels  generated  within
 conditional  assembly  blocks,  and  so  on.   The ASM statements
 provide these capabilities.  The most often used ASM statement is
 the ASM IF:
 
      ASM IF (condition) THEN statement ELSE statement
 
 where the "ELSE" clause is optional.
 
 
 
 Examples:
 
      ASM IF ('&TYPE' EQ 'EMPTY') THEN statement;
 
 translates to:
 
        AIF (NOT ('&TYPE' EQ 'EMPTY')).@0001
        statement
 .@0001 ANOP
 
 
 
      ASM IF (&&V EQ &&X) THEN statement1 ELSE statement2;
 
 generates:
 
        AIF (NOT (&V EQ &X)).@0001
        statement1
        AGO .@0002
 .@0001 ANOP
        statement2
 .@0002 ANOP
 
 
 
 NOTE:  If "statement1" in the "...  THEN ...  ELSE ..." form is a
 simple statement without operands (e.g.   a  macro  call  without
 operands,  an  assembler  op-code without operands, etc.) then it
 should be bracketed with '<'/'>' symbols to  prevent  the  'ELSE'
 from being interpreted as an operand of the statement.
1                           - 24 -
 
 
 Most other ALP statements are available in the  ASM  form  in  an
 analogous way.
 
 . ASM WHILE (condition) DO statement THEN statement
 . ASM UNTIL (condition) DO statement THEN statement
 . ASM DO statement WHILE (condition) THEN statement
 . ASM DO statement UNTIL (condition) THEN statement
 . ASM DO statement THEN statement
 . ASM FOREVER DO statement
 . ASM DO statement FOREVER
 . ASM CASE set-expression;
      case-list: statement;
      ...
      ENDCASE
   THEN statement
 . ASM CASE set-expression;
      case-list: statement;
      ...
      ENDCASE
   ELSE statement
   THEN statement
 . ASM SELECT;
      (condition): statement;
      ...
      ENDSEL
   THEN statement
 . ASM SELECT FIRST;
      (condition): statement;
      ...
      ENDSEL
   THEN statement
 . ASM SELECT FIRST;
      (condition): statement;
      ...
      ENDSEL
   ELSE statement
   THEN statement
 . ASM FOR seta-variable FROM seta-expression BY seta-expression
     TO seta-expression DO statement THEN statement
 . ASM DO statement FOR seta-variable BY seta-expression
     TO seta-expression THEN statement
 . ASM EXIT
 . ASM EXIT FROM sequence-symbol
 . ASM EXIT IF (condition)
 . ASM EXIT FROM sequence-symbol IF (condition)
 . ASM NEXT
 . ASM NEXT OF sequence-symbol
 . ASM NEXT IF (condition)
 . ASM NEXT OF sequence-symbol IF (condition)
 . ASM GOTO sequence-symbol
 . ASM GOTO sequence-symbol IF (condition)
1                           - 25 -
 
 
 Notable points are
 
 . "condition" represents a valid SETB expression.
 . the THEN clause is optional with all statements except ASM IF.
 . FROM, BY and TO are provided with ASM FOR to define the  limits
   of the loop.  The defaults are 1, 1 and infinity, respectively.
   If   negative  numbers  are  used,  they  must  be  written  as
   "0-number", in honor of  the  assembler  restriction  on  unary
   operators.  FROM is not valid with ASM DO FOR.
 . The selection value in the ASM CASE statement  may  also  be  a
   SETC   expression  in  quotes.   If  this  is  done,  the  case
   identifiers must also be SETC expressions in quotes.
 . MAX and MIN are not used with ASM CASE.
 . There is no ASM RGOTO statement.
 . ASM IF may also be written  as  ASMIF  for  compatability  with
   earlier versions.
1                           - 26 -
 
 INCLUDING ALP CODE IN MACROS
+____________________________
 
      Although macros are  frequently  used  for  describing  data
 structures or for small common code segments containing little or
 no  control  structure,  this  is  not  always the case.  In such
 instances it is desirable to  write  them  in  ALP  in  order  to
 continue  to maintain consistency and preserve the goals of using
 a  structured  language.   ALP's  MACRO  statement   allows   the
 definition  of assembler macros which may contain ALP constructs.
 Its format is:
 
      MACRO  macro-label: macro-name macro-operands;
         GBLx and LCLx declarations
         macro-body
         MEND
 
 where:
 
      macro-label is the (optional) label to be placed on
      the first statement of the macro, and is of the form
      &&identifier
 
      macro-name is the name of the macro
 
      macro-operands is an (optional) operand field which
      names the symbolic operands of the macro, in the form
      &&identifier,&&identifier,...
 
 
 Example:
 
      MACRO &&LABEL: ZAP &&P1,&&P2;
         GBLA &&X;
         COPY NAMES;
         &&LABEL: IF <RP &&P1> THEN <ZR &&P1>
         ELSE <LCR &&P2,&&P1>;
         MEND;
 
 generates
 
          MACRO
 &LABEL   ZAP   &P1,&P2
          GBLA  &X
          COPY  NAMES
          LCLC  &@
 &@       SETC  '&SYSNDX'
 &LABEL   LTR   &P1,&P1
          BNP   @&@001
          SR    &P1,&P1
          B     @&@002
 @&@001   LCR   &P2,&P1
 @&@002   ...
 
 
 NOTE:   The  doubling  of  ampersands  ('&')  is  necessary,   as
 described  in section II, to prevent confusion with the predicate
 operator "AND".
1                           - 27 -
 
 
      All GBLx and LCLx declarations and any COPY statements which
 copy in such statements must be  grouped  immediately  after  the
 MACRO header.  This is because a local set symbol must be defined
 so that ALP-generated labels do not result in duplicate labels if
 a  macro  is  invoked  more  than  once.   Assembler restrictions
 require  that  all  set   symbol   declarations   precede   other
 statements,  and  ALP  picks the point at which to define its own
 set symbol by detecting the first statement which is not a  GBLx,
 LCLx,  or COPY.  Another consequence of this is that a COPY which
 copies in executable code MUST be preceded by a  dummy  statement
 of some sort to prevent premature generation of the ALP local set
 symbol.  For example:
 
      MACRO EXAMPLE;
         GBLA &&X;
         ; % TO FOOL ALP
         COPY CODE; % TO COPY IN EXECUTABLE CODE
         MEND;
 
 
 ALP may also be used to process macros to be stored in  assembler
 macro  libraries.   To  facilitate  this,  ALP  will pass through
 unchanged any ./ control cards which occur in the  input  stream.
 Thus, output from ALP may be passed directly to IEBUPDTE.
1                           - 28 -
 
 REVERSION TO BAL
+________________
 
      While  most  assembler  code  can  be  written  within   the
 framework  of  ALP, it may occasionally be necessary to revert to
 BAL mode.  The ALP statement "BAL;" will cause  the  preprocessor
 to  enter  a  transparency  mode, in which card images are simply
 copied from the input stream to the output stream.  BAL  mode  is
 terminated when "ALP;" appears as the first non-blank symbol on a
 line.  Any text beyond the "BAL;" on the same  line  is  ignored.
 The format of the statement is:
 
      BAL;
      bal-code
      ALP;
 
 
 
 Examples:
 
      BAL;
           MACRO
      &L   ADD   &A,&B,&C
           L  15,&A
           A  15,&B
           ST 15,&C
           MEND
      ALP;
 
 
      BAL;
       IF  &L1,&L2
      ALP;
1                           - 29 -
 
 BLOCK COMMENTS
+______________
 
      The comment statement is an alternate  way  of  including  a
 large block of comments in an ALP program.  All lines following a
 "COMMENT;"  statement  are ignored.  Normal processing is resumed
 when "ALP;" appears as the first non-blank character on  a  line.
 The  advantage  of  COMMENT over normal comments is that WYLBUR's
 ALIGN and JUSTIFY  commands  may  be  used  since  there  are  no
 extraneous characters on the comment lines.
 
 Example:
 
      COMMENT;
 
      Normally a long-winded  explanation  of  some  part  of  the
      program would appear here.
 
      ALP;
1                           - 30 -
 
 
 LISTING FORMAT CONTROL
+______________________
 
      Several conventions were adopted to  allow  control  of  the
 SYSPRINT  listings  of  both ALP and the assembler.  These are as
 follows:
 
 . The indentation of each line is automatically adjusted to be  3
   times  the nesting level at the start of the line.  The nesting
   level is the number of unterminated BEGIN, <, CASE, SELECT  and
   MACRO statements.
 
 . Blank lines are ignored by ALP, and may thus be used to  format
   input  source.   They  are  not passed on to the assembler, and
   hence have no effect on its output.
 
 . If ALP is being used  in  conjunction  with  the  assembler,  a
   post-processor   extracts  location  counter  values  from  the
   assembler listing and adds them to the ALP listing.   In  order
   for this process to work properly,  the  input  lines  must  be
   sequence  numbered in ascending order in columns 73 through 80.
   Special care must be taken  with  COPY  statements  outside  of
   macros as they will disrupt the sequencing.  Sequence fields of
   all  blanks  or all zeroes are ignored.  The IEBUPDTE statement
   ./ NUMBER NEW1=0,INCR=0 may be used to cause  sequence  numbers
   of all zeroes to be placed in a COPY module.
 
 . ALP provides limited support for the assembler directive SPACE.
   The  ALP  listing  is  arbitrarily spaced up two lines, and the
   SPACE and its operands (if any -- no checking for  validity  is
   performed) are passed on to the assembler.
 
 . ALP processes the EJECT assembler directive by causing  a  page
   eject and passing the EJECT (and any operands -- no checking is
   done) on to the assembler.
 
 . ALP accepts the assembler directive TITLE.   The  operands  are
   stored for printing at the top of each page, and with the TITLE
   op-code  are  passed on to the assembler.  No validity checking
   is performed, but there should be only one operand -- a  quoted
   string.   If  a  label  is  present,  it  is also passed to the
   assembler.  Note that there is an  assembler  requirement  that
   only  one  such  "deck  name"  be present in any assembly.  The
   default title is a standard ALP heading.
 
 . ALP supports a SUBTITLE statement.  The operands, which  should
   consist  of  a single quoted string, are stored for printing at
   the top of each page immediately below the current title.   The
   SUBTITLE  is converted to a TITLE directive and passed with its
   operands to the assembler.  The default  subtitle  is  a  blank
   line.
 
 . ./ (IEBUPDTE) control cards cause a page eject.
1                           - 31 -
 
 
 NOTE:  SPACE, EJECT, TITLE,  and  SUBTITLE  are  all  treated  as
 regular  assembly  language  statements  --  no special notice is
 taken that they also influence formatting of the source listings.
 Hence some care must be taken in their placement in  the  source.
 For example,
 
          IF predicate THEN BEGIN
             statements
             END
          ELSE
          EJECT;
          BEGIN
             statements
             END;
 
 will cause the EJECT to form the body of the ELSE clause and  not
 the  desired  BEGIN-END  block.   It  is  also not permissible to
 separate  CASE  or  SELECT   components   with   format   control
 statements.
1                           - 32 -
 
 
                    IV. NON-CONTROL EXTENSIONS
 
 
     Some non-control extensions are provided by ALP in an attempt
 to improve the conceptual environment in which  one  programs  at
 the  assembly language level.  There are several notions that are
 fairly well established in the machine instruction  set  and  the
 basic assembly language.  These include word, halfword, byte, and
 register  operations.   A  very  important data type not directly
 covered is the bit.  Bit operations  are  adequately  handled  by
 byte  instructions, but what is missing is a clear identification
 that one is dealing  with  bits.   AL  provided  three  'extended
 mnemonics',  TB,  SB, and ZB for test bit, set bit, and zero bit.
 These allowed writing code as if  the  machine  had  instructions
 with  byte  and  bit addressing rather than having to think about
 the  appropriate  mask  to  use  with  a   particular   kind   of
 instruction.   However,  there  were  several  problems with this
 approach, and we decided that the ability to use symbolic  masks,
 etc.   was  more  important.   Hence  these  macros  appear  in a
 modified form or not at all.
 
     A very important set of instructions in the 360/370  are  the
 byte  string instructions.  Unfortunately, the notion provided at
 the BAL level is rather poor.  One problem  is  that  the  length
 field  in  the instruction is one less than the effective length.
 Another problem is that the BAL format confuses the length  field
 with  the  base register field of the first operand.  This latter
 problem is  solved  by  separating  out  the  length  field.   AL
 provided  the  MOVE  instruction  instead  of  MVC  and  the COMP
 instruction instead  of  CLC;  these  names  also  emphasize  the
 importance  and  generality  of  these  instructions  rather than
 confusing one  with  "logical  character".   Since  ALP  provides
 extended macros for more than just MVC and CLC, we elected to use
 mnemonics  closer to the original ones.  Note that these extended
 facilities provide more than just modification of the format.
 
     Certain  other  operations  are  clarified  with  appropriate
 mnemonics.  For example:  ZR (for Zero Register),  RP,  RZ,  etc.
 for Register Plus, Zero, and so on (all generate an LTR but imply
 different condition code tests), and ZI (for Zero Immediate -- an
 NI   with   255-bitvalue   mask).    Macros  useful  in  ALP  for
 clarification purposes are listed below.  Not  all  are  actually
 required (see the end of section II for those that are built into
 the  translator), but all have been found useful.  Note that some
 AL macros have been changed or replaced, and others (due  to  our
 own preferences) discarded.
1                           - 33 -
 
 
       AI - Add Immediate
       CI - Compare Immediate
      CIL - Compare Immediate Logical
       DI - Divide Immediate
       LI - Load Immediate
      LQS - Load Quoted String
       LT - Load and Test
       MI - Multiply Immediate
       RM - Register Minus
      RMP - Register Minus or Plus
      RMZ - Register Minus or Zero
      RNM - Register Not Minus
     RNMP - Register Not Minus or Plus
     RNMZ - Register Not Minus or Zero
      RNP - Register Not Plus
      RNZ - Register Not Zero
     RNZP - Register Not Zero or Plus
       RP - Register Plus
       RZ - Register Zero
      RZP - Register Zero or Plus
       SI - Subtract Immediate
        Z - Zero
       ZB - Zero Byte
       ZH - Zero Halfword
      ZHB - Zero High Byte
     ZHBR - Zero High Byte Register
       ZI - Zero Immediate
       ZR - Zero Register
      EXI - Execute immediate
     EDIT - Generate edit mask and ED/EDMK instruction
     MCLC - Multiple Compare Logical Characters
     MMVC - Multiple Move Characters
      MNC - Multiple AND Characters
      MOC - Multiple OR Characters
      MXC - Multiple Exclusive-OR Characters
      MFC - Multiple Fill Characters
      MTR - Multiple Translate
     MTRT - Multiple Translate and Test
      MZC - Multiple Zero Characters
       DF - Define Flags
       SF - Set Flags
       TF - Test Flags
       ZF - Zero Flags
  DEBLANK - Deblank a string
    OPENP - Check for successful open
 
      See sections VII and VIII for  further  information  on
 these macros.
1                           - 34 -
 
 
                   V. THE IMPLEMENTATION OF ALP
 
 
      ALP has been implemented as a preprocessor to  the  standard
 OS/360  assembler,  using  macros  within  the  assembler in some
 instances to enhance readability.  The preprocessor is written in
 PL/I using recursive descent, and  is  approximately  3100  lines
 long.   The post-processor for extracting location counter values
 is also written in PL/I and is approximately 365 lines long.
 
      ALP,  the  assembler  and  the  post-processor  are  usually
 invoked in sequence by a small control program, allowing the  two
 tasks  to be executed as one job step.  Cataloged procedures (see
 section XI) have been developed for using ALP.
1                           - 35 -
 
 
                        VI. ALP SYNTAX
 
 
                           Notation
 
 
 
 Non-terminal  symbols  are  lower  case  identifiers  (which  may
 include a "dash")
 
 Terminal symbols are either upper  case  identifiers  or  special
 symbols enclosed in quotation marks
 
 ->     means "is defined as"
 
 |      indicates alternatives
 
 "  "   means must be entered as is
 
 (  )   indicates an optional occurrence (0 or 1 times)
 
 (  )*  indicates multiple optional occurrences (0 or more times)
 
 <  >   indicates a required selection  of  one  of  the  enclosed
        alternatives
 
 <  >*  indicates a required selection  of  one  or  more  of  the
        enclosed alternatives
 
 
 
 Some non-terminals are left undefined.  Their meaning  should  be
 obvious from their names.
1                           - 36 -
 
 
 program -> statements ";" END ";"
 
 statements -> statement (";" statement)*
 
 statement -> (label ":")* <compound-statement | simple-statement>
 
 compound-statement -> "<" statements ">"
                     | BEGIN  statements  END
 
 simple-statement -> if | case | select | loop | goto | exit | next
                   | mapping | data | conditional-assembly | macro
                   | format-control | bal | cc | bal | comment
 
 
 if -> IF predicate THEN statement (ELSE statement)
 
 
 case -> CASE  register-id  (case-option)* ";"
         case-list
         ENDCASE
         (ELSE statement)
         (THEN statement)
 
 case-option -> MAX expression
              | MIN expression
              | CHECK
 
 case-list -> <case-label-list ":" statement ";">*
 case-label-list -> case-label ("," case-label)*
 case-label -> expression (THRU expression)
 
 
 select -> SELECT (FIRST) ";"
           selection-list
           ENDSEL
           (ELSE statement)
           (THEN statement)
 
 selection-list -> <predicate ":" statement ";">*
 
 
 loop -> <WHILE | UNTIL> predicate DO statement (THEN statement)
       | DO statement <WHILE | UNTIL> predicate (THEN statement)
       | FOR register-id DO statement (THEN statement)
       | DO statement FOR register-id (THEN statement)
       | DO statement (THEN statement)
       | FOREVER DO statement
       | DO statement FOREVER
 
 
 goto -> <GOTO | RGOTO> target (IF predicate)
 
 
 exit -> EXIT (FROM label) (IF predicate)
1                           - 37 -
 
 
 
 next -> NEXT (OF label) (IF predicate)
 
 
 mapping -> USE register AS dsect-id ("," register AS dsect-id)*
            IN statement
 
 data -> DATA statement
 
 conditional-assembly -> asm-if | asm-case | asm-select | asm-loop
                       | asm-goto | asm-exit | asm-next
 
 asm-if -> ASM IF setb-expression THEN statement (ELSE statement)
 
 asm-case -> ASM CASE set-expression ";"
             asm-case-list
             ENDCASE
             (ELSE statement)
             (THEN statement)
 
 asm-case-list -> <asm-case-label-list ":" statement ";">*
 asm-case-label-list -> asm-case-label ("," asm-case-label)*
 asm-case-label -> set-expression (THRU set-expression)
 
 asm-select -> ASM SELECT (FIRST) ";"
               asm-selection-list
               ENDSEL
               (ELSE statement)
               (THEN statement)
 
 asm-selection-list -> <setb-expression ":" statement";">*
 
 asm-loop -> ASM <WHILE | UNTIL> setb-expression
             DO statement (THEN statement)
           | ASM DO statement <WHILE | UNTIL> setb-expression
             (THEN statement)
           | ASM FOR seta-variable (FROM seta-expression)
             (BY seta-expression) (TO seta-expression)
             DO statement (THEN statement)
           | ASM DO statement FOR seta-variable (BY seta-expression)
             (TO seta-expression) (THEN statement)
           | ASM DO statement (THEN statement)
           | ASM FOREVER DO statement
           | ASM DO statement FOREVER
 
 asm-goto -> ASM GOTO sequence-symbol (IF setb-expression)
 
 asm-exit -> ASM EXIT (FROM sequence-symbol) (IF setb-expression)
 
 asm-next -> ASM NEXT (OF sequence-symbol) (IF setb-expression)
 
 macro -> MACRO (macro-label) macro-name (macro-operands)
 
 macro-label -> "&&"label":"
 
 macro-operands -> "&&"identifier (",&&"identifier)*
1                           - 38 -
 
 
 format-control -> EJECT
                   SPACE ( integer )
                   TITLE "'" title "'"
                   SUBTITLE "'" subtitle "'"
 
 
 bal ->  BAL;
         bal-segment
         ALP;
 
 comment ->  COMMENT;
             text
             ALP;
 
 cc ->  CC  condition-code-string
 condition-code-string -> <N | "^" | 0 | "=" | E | Z | 1 | L | M |
                            2 | P | H | 3 | O>*
 
 
 predicate -> ("^")* <statement | "<" predicate ">">
            | predicate "&" predicate
            | predicate "|" predicate
 
 
 comment ->  "%" text "end-of-line"
1                           - 39 -
 
 
                  VII.  ALP READABILITY MACROS
 
 
 In the description that follows,
 
     r  is a register
     a  is any relocatable expression that is valid in an
        instruction
     c  is a constant
 
 
 Macro             Name                     Code Generated
 
 AI   r,c          Add Immediate            LA   r,c(,r)
 
 AI   0,c          Add Immediate            AL   0,=A(c)
 
 
 CI   r,c          Compare Immediate        C    r,=A(c)
 
 CIL  r,c          Compare Immediate        CL   r,=A(c)
                   Logical
 
 DI   r,c          Divide Immediate         D    r,=A(c)
 
 LI   r,c          Load Immediate           LA   r,c
 
 LQS  rx,ry,'str'  Load Quoted String       LA   rx,=C'str'
                                            LA   ry,length
 
 LT   r,a          Load and Test            L    r,a
                                            LTR  r,r
 
 MI   r,c          Multiply Immediate       MH   r,=AL2(c)
 
 RM   r            Register Minus           LTR  r,r
 
 RMP  r            Register Minus or Plus   LTR  r,r
 
 RMZ  r            Register Minus or Zero   LTR  r,r
 
 RNM  r            Register Not Minus       LTR  r,r
 
 RNMP r            Register Not Minus       LTR  r,r
                   or Plus
 
 RNMZ r            Register Not Minus       LTR  r,r
                   or Zero
 
 RNP  r            Register Not Plus        LTR  r,r
 
 RNZ  r            Register Not Zero        LTR  r,r
 
 RNZP r            Register Not Zero        LTR  r,r
                   or Plus
1                           - 40 -
 
 
 
 RP   r            Register Plus            LTR  r,r
 
 RZ   r            Register Zero            LTR  r,r
 
 RZP  r            Register Zero or Plus    LTR  r,r
 SI   r,1          Subtract Immediate       BCTR r,0
 
 SI   r,2          Subtract Immediate       BCTR r,0
                                            BCTR r,0
 
 SI   r,c          Subtract Immediate       SL   r,=A(c)
 
 Z    r,a          Zero                     SR   r,r
                                            ST   r,a
 
 Z    ,a           Zero                     XC   a(4),a
 
 ZB   r,a          Zero Byte                SR   r,r
                                            STC  r,a
 
 ZB   ,a           Zero Byte                MVI  a,0
 
 ZH   r,a          Zero Halfword            SR   r,r
                                            STH  r,a
 
 ZH   ,a           Zero Halfword            XC   a(2),a
 
 ZHB  a            Zero High Byte           MVI  a,0
 
 ZHBR r            Zero High Byte Register  LA   r,0(,r)
 
 ZHBR 0            Zero High Byte Register  N    0,=XL4'00FFFFFF'
 
 ZI   a,c          Zero Immediate           NI   a,255-(c)
 
 ZR   r            Zero Register            SR   r,r
1                           - 41 -
 
 
            VIII. Macros for Environment Enhancement
 
 
                         Conventions
 
 
 
 
 Macro operands are described using the following terms:
 
    cexpr4     - denote expressions which evaluate to  a  constant
                 to be held in 4 bits
 
    cexpr8     - denote expressions which evaluate to  a  constant
                 to be held in 8 bits
 
    relexpri   - denotes a relocatable expression that is valid as
                 a storage address in an instruction
 
    symbol     - an identifier acceptable to the assembler
 
    reg        - any register
 
    preg       - any register except 0
1                           - 42 -
 
 
   AREA, AREAORG and AREAEND - Define a structured storage area
+  ____________________________________________________________
 
 
 
 
 AREA and AREAEND are used to define an area of storage  which  is
 structured  into  smaller  named  components.   AREA  begins  the
 definition,  DSs  and  DCs  follow,  and  AREAEND  terminates the
 definition.
 
 AREAORG is used to ORG back to the start  of  the  area  so  that
 fields  may  be  overlaid.   The  length  of the area will be the
 maximum attained.
 
 
 
 <symbol> AREA alignment<,DSECT=NO>
 
 
 
     symbol               symbol
 
         The name of the total storage area.  The length attribute
         will be correctly set.
 
 
     alignment            X,H,F,D,0X,0H,0F,0D
 
         Specifies the boundary alignment for the  area.   Default
         is X (byte alignment).
 
 
     DSECT=NO
 
         Indicates that the area is not to be a DSECT.
 
 
 
 <symbol> AREAEND <alignment>
 
 
 
     symbol               symbol
 
         A symbol which is to be EQUed to the length of the area.
 
 
 
     alignment            X,H,F,D,0X,0H,0F,0D
 
         Specifies the boundary alignment for the end of the area.
         Default is what was specified in the AREA macro.
1                           - 43 -
 
 
 
 <symbol> AREAORG <alignment>
 
 
 
     symbol               symbol
 
         A symbol which is to be EQUed to the  current  length  of
         the area.
 
 
     alignment            X,H,F,D,0X,0H,0F,0D
 
         Specifies boundary alignment for the end of this  overlay
         of  the  area.  Default is what was specified in the AREA
         macro.
 
 
 
 NOTE:
 
    Area definitions may be nested.  DSECT=NO is  implied  at  the
    inner levels.
 
 
 
 EXAMPLE:
 
     WA      AREA     F
     WATEMP  DS       F
     WABYTE  DS       X
     WAHALF  DS       H
     WASIZE  AREAEND
1                           - 44 -
 
 EXAMPLE:
 
     WA       AREA     F
     WATEMP   DS       F
     WA2      AREA     D
     WABYTE   DS       X
     WAHALF   DS       H
     WA2SIZE  AREAEND
     WAHALF2  DS       H
     WASIZE   AREAEND
 
        generates
 
     WA       DSECT
     WATEMP   DS       F
     WA2      DS       OD
     WABYTE   DS       X
     WAHALF   DS       H
              DS       OD
     WA2SIZE  EQU      *-WA2
     WAHALF2  DS       H
              DS       OF
     WASIZE   EQU      *-WA
     prevsect CSECT
 
     where "prevsect" is the previous CSECT name
1                           - 45 -
 
 
 
                    DEBLANK - Deblank a string
+                   __________________________
 
 
 
 
 The DEBLANK macro removes leading and/or trailing blanks  from  a
 string.
 
 
 
 <symbol> DEBLANK loc-reg,len-reg<,work-reg><,TYPE=symbol>
                <,NULL=NO><,ZERO=NO><,LABEL=symbol><,FILL=char>
                <,FILADDR=byte>
 
 
 
     loc-reg              preg
 
         Specifies the  starting  address  of  the  string  to  be
         deblanked.
 
 
     len-reg              reg
 
         Specifies the length  of  the  string  to  be  deblanked.
         After  the  termination  of the macro, this register will
         contain the new length of the deblanked string.
 
 
     work-reg             preg
 
         Provides a work register to be used in the search.   More
         efficient  code  may  be  generated  if  this register is
         provided.
 
 
     TYPE=symbol          LEFT, RIGHT, or BOTH
 
         Specifies  elimination  of  leading  (LEFT)  or  trailing
         (RIGHT) blanks, or both (BOTH).  Default is RIGHT.
 
 
     NULL=NO
 
         The NO condition specifies that the resulting string will
         never be 0.  More efficient code may be generated if this
         option is specified.
 
 
     ZERO=NO
 
         The NO condition specifies that  the  value  in  the  len
         register  will  never  be  0.  More efficient code may be
         generated if this option is specified.
1                           - 46 -
 
 
 
     LABEL=symbol         relexpri
 
         The location to receive control if the  resulting  string
         has a length of zero.
 
     FILL=char            cexpr8
 
         Used to specify  a  character  other  than  blank  to  be
         stripped.
 
     FILADDR=byte         relexpri
 
         Used to specify the  location  of  the  character  to  be
         stripped.  May not be used with FILL.
 
 
 RETURNS:
 
     loc-reg =  location of deblanked string
 
     len-reg =  length of deblanked string
1                           - 47 -
 
 
        EDIT - Generate edit mask and ED/EDMK instruction
+       _________________________________________________
 
 
 
 
 EDIT is used to create both an appropriate mask string or editing
 numeric data and the  ED  or  EDMK  instruction  to  perform  the
 requested operation.
 
 
 
 <symbol> EDIT to-field,from-field<,to-length><,from-length>
               <,CALC=NO><,DIGITS=n><,MARK=YES>
 
 
 
     to-field             relexpri or (preg)
 
         The address of the field to  contain  the  edited  source
         digits.  It must be an even number of bytes in length.
 
 
     from-field           relexpri or (preg)
 
         The address of the field containing the source digits  to
         be  EDITed  to  the to-field.  It must contain sufficient
         digits to satisfy the implicit (or  explicit)  length  of
         the to-field.
 
 
     to-length            cexpr4
 
         An explicit specification of the length of the  to-field.
         It  must  be  specified  if  the to-field is presented in
         base-displacement form.  If specified  it  will  override
         the implicit length for the to-field.
 
 
     from-length          cexpr4
 
         An  explicit  specification  of   the   length   of   the
         from-field.   It  must  be specified if the from-field is
         specified in base-displacement  form.   If  specified  it
         overrides the implicit length for the from-field.
 
     CALC=NO
 
         Indicates that the addresses specified  are  to  be  used
         exactly  as  is  for  the  from-  and  to-fields  in  the
         generated  ED  or EDMK instruction.  If not specified the
         macro will calculate the offset in the from-field to  use
         in the ED or EDMK instruction.
1                           - 48 -
 
 
     DIGITS=n             cexpr4
 
         Specifies the minimum number of significant digits to  be
         produced.
 
     MARK=YES
 
         Indicates that an EDMK instruction should  be  generated.
         Register  1  will  then  point  to  the first significant
         character in the edited field.  If  the  field  does  not
         produce a significatn digit, register 1 will point to the
         low order character of the edited field.
1                           - 49 -
 
 
                EXI and EXORG - Execute immediate
+               _________________________________
 
 
 
 
 EXI permits the instruction to be executed by an  EX  instruction
 to be coded at the same place in the source program.
 
 
 
 <symbol> EXI ex-reg,opcode,operand1,operand2,<DECR=YES>,
              <INCR=YES>
 
 
 
     ex-reg               reg
 
         The register to be used as the first operand  of  the  EX
         instruction.
 
 
     opcode               valid assembler opcode
 
         Operation code of the instruction to be executed.
 
 
     operand1
 
         The first operand of the instruction to be executed.
 
 
     operand2
 
         The second operand of the instruction to be
         executed.
 
 
     DECR=YES
 
         Specifies that the register is to be decremented  by  one
         before the EX instruction.
 
     INCR=YES
 
         Specifies that the register is to be incremented  by  one
         after  the  EX  instruction.   The  condition code is not
         affected.
1                           - 50 -
 
 
 
 NOTES:
 
     1.  The opcode to be executed may not be a macro unless it is
         one of the following:  MCLC, MMVC, MNC,  MOC,  MTC,  MTR,
         MTRT,  MXC,  MZC.   When  one of these is used, N=1 and a
         length of zero are forced.
 
     2.  An EXORG must be included  within  addressable  range  in
         order to assemble the instructions to be executed.
 
     3.  If an instruction  occurs  more  than  once,  EXORG  will
         assemble only one copy.
1                           - 51 -
 
 
 
                    Extended Length Facilities
+                   __________________________
 
 
 
 
 These macros generate inline  code  to  provide  extended  length
 facilities.  These macros provide an optional N=count  operand to
 allow  the  writer to specify the exact number of instructions to
 be generated.  If   N=count   is  not  present,  and  the  length
 operand  is  an  unsigned  integer or a SETA symbol, then as many
 instructions as are required for the  specified  length  will  be
 generated.  If  N=count  is not present and the length operand is
 not  an  unsigned integer or SETA symbol, then one instruction is
 generated.
 
 
 
                MCLC, MMVC, MNC, MOC, and MXC
 
 
 
 <symbol> opcd  oper1,oper2,length<,N=count><,ZERO=NULL>
 
 
 
     opcd                 MCLC, MMVC, MNC, MOC, or MXC
 
 
     oper1                relexpri or (preg)
 
         The address of the 1st operand.
 
 
     oper2                relexpri or (preg)
 
         The address of the 2nd operand.
 
 
     length
 
         The number of bytes affected.
 
 
     N=count              unsigned integer or SETA symbol
 
         The number of instructions to be generated.
 
     ZERO=NULL
 
         Specifies that no instructions are to be generated if len
         is  zero.   Normally  a  single  instruction   would   be
         generated.
1                           - 52 -
 
 
                        MFC - Fill a field
+                       __________________
 
 
 
 
 The MFC macro will fill a field with the specified charater.
 
 
 
 <symbol> MFC   loc,len<,FILL=char><,N=count><,ZERO=NULL>
 
 
 
     loc                 relexpri or (preg)
 
         The address of the field to be filled.
 
 
     len
 
         The length of the field to be filled.
 
 
     FILL=char            cexpr8
 
         The character to fill the field with.  Default is
         blank (C' ')
 
 
     N=count              unsigned integer or SETA symbol
 
         The number of instructions to be generated.
 
     ZERO=NULL
 
         Specifies that no instructions are to be generated if len
         is zero.
1                           - 53 -
 
 
                        MTC - Test a field
+                       __________________
 
 
 
 
 MTC tests a field for all zero (or other specified value) bytes.
 
 
 
 <symbol> MTC loc,len<,FILL=char><,N=count><,ZERO=NULL>
 
 
 
     loc                  relexpri or (preg)
 
         Address of field to be tested.
 
 
     len
 
         Length of field.
 
 
     FILL=char            cexpr8
 
         The character to be tested for.  Default is 0.
 
 
     N=count              unsigned integer or SETA symbol
 
         Number of instructions to be generated.
 
     ZERO=NULL
 
         Specifies that no test is to be performed if len is zero.
         The condition code will be set to zero in that case.
 
 
 
 NOTE:
 
     If FILL is not specified, OC instructions  are  generated  to
     test  the  field  for  zeros.   If  FILL  is  specified,  CLC
     instructions are generated, even if FILL=0 is specified.
1                           - 54 -
 
 
                     MTR - Translate a field
+                    _______________________
 
 
 
 
 MTR translates a field using a specified translate table.
 
 
 
 <symbol> MTR loc,table,len<,N=count><,ZERO=NULL>
 
 
 
     loc                  relexpri or (preg)
 
         Location of field to be translated.
 
 
     table                relexpri or (preg)
 
         Location of translate table.
 
 
     len
 
         Length of field.
 
 
     N=count              unsigned integer or SETA symbol
 
         Number of TR instructions to be generated.
 
     ZERO=NULL
 
         Specifies that no instructions are to be generated if len
         is zero.
1                           - 55 -
 
 
                MTRT - Translate and test a field
+               _________________________________
 
 
 
 
 MTRT performs a translate-and-test on a field.
 
 
 
 <symbol> MTRT loc,table,len<,N=count><,ZERO=NULL>
 
 
 
     loc                  relexpri or (preg)
 
         Location of field.
 
 
     table                relexpri or (preg)
 
         Location of translate-and-test table.
 
 
     len
 
         Length of field.
 
 
     N=count              unsigned integer or SETA symbol
 
         Number of instructions to be generated.
 
     ZERO=NULL
 
         Specifies that no translate and test is to  be  performed
         if  len  is  zero.   The condition code is set to zero in
         that case.
1                           - 56 -
 
                       MZC - Clear a field
+                      ___________________
 
 
 
 
 The MZC macro will clear a field to all X'00's.
 
 
 
 <symbol> MZC   loc,len<,N=count><,ZERO=NULL>
 
 
 
     loc                 relexpri or (preg)
 
         The address of the field to be zeroed.
 
 
     len
 
         The length of the field to be zeroed.
 
 
     N=count              unsigned integer or SETA symbol.
 
         The number of instructions to be generated.
 
     ZERO=NULL
 
         Specifies that no instructions are to be generated if len
         is zero.
1                           - 57 -
 
                        DF - Define flags
+                       _________________
 
 
 DF is used to define one or more flag bits and optionally  assign
 initial values.
 
 <symbol> DF flag-name,...<INIT=(flag-name,...)>
 
 
     flag-name            symbol
 
        The name of the flag to be defined.  Any number  of  flags
        may be specified.  If more than 8 are specified, more than
        1 byte will be reserved.
 
     INIT=(flag-name,...) list of symbols
 
        Specifies flags which are to be initially 1 (on).
1                           - 58 -
 
                          SF - Set flags
+                         ______________
 
 
 SF is used to turn on one or more flags defined with DF.
 
 <symbol> SF flag-name,...
 
 
     flag-name            symbol
 
        The name of a flag to be turned on (set to 1).   Up  to  8
        flags may be specified; all must reside in the same byte.
1                           - 59 -
 
                         TF - Test flags
+                        _______________
 
 
 TF is used to test one or more flags defined with DF.
 
 <symbol> TF flag-name,...
 
 
     flag-name            symbol
 
        The name of a flag to be tested.  Up to  8  flags  may  be
        specified; all must reside in the same byte.
 
 
 RETURNS:
 
     CC =  Z  all tested flags off
           O  all tested flags on
           M  some on, some off
1                           - 60 -
 
                         ZF - Zero flags
+                        _______________
 
 
 ZF is used to turn off one or more flags defined with DF.
 
 <symbol> ZF flag-name,...
 
 
     flag-name            symbol
 
        The name of a flag to be cleared.  Up to 8  flags  may  be
        specified; all must reside in the same byte.
1                           - 61 -
 
          OSCALL - Pass control to an OS-type subroutine
+         ______________________________________________
 
 
 The OSCALL macro will pass  control  to  a  specified  subroutine
 using OS calling conventions.
 
 <symbol> OSCALL routine<,A><,R1=parm><,R0=parm>
                 <,R15=parm>
 
 
     routine              relexpra or vsymbol or (preg)
 
        The address of the subroutine to be called.
 
     A
 
        The address  specified  in  the  routine  parameter  is  a
        relexpra.
 
     R1=parm             addrla
 
        A parameter to be passed in register 1.
 
     R0=parm             addrla
 
        A parameter to be passed in register 0.
 
     R15=parm             addrla
 
        A parameter to be passed in register 15.
 
 
 NOTE:
 
    Register 15 is loaded with  the  entry  point  address  unless
    R15=parm is specified
1                           - 62 -
 
                 OSENTER - Generate OS entry code
+                ________________________________
 
 
 The OSENTER macro will generate proper OS entry linkage code.
 
 <symbol> OSENTER <(reg1,reg2),...><,ENTRY=NO>
                  <,BASE=NO><,SAVE=area><,PACK=YES>
                  <,FORWARD=YES><,ID=identification>
 
 
     reg1,reg2            regs
 
        Registers  to  be  saved  in  STM  form.   Any  number  of
        parenthesized pairs may be specified.  If reg2 is the same
        as reg1, then reg2 and the parentheses may be omitted.
 
     ENTRY=NO
 
        Requests that an ENTRY point not be generated.
 
     BASE=NO
 
        Requests that a base register not be established.
 
     SAVE=area            relexpri
 
        The address of the users register save area.
 
     PACK=YES
 
        Registers are to be stored packed at 12  bytes  after  the
        start of the save area.
 
     FORWARD=YES
 
        Specifies that the forward linking of save areas is to  be
        performed.  Normally only backward linking is done.
 
     ID=identification    symbol or string or *
 
        Specifies an identifying character string to be  assembled
        4 bytes after the entry point.  * indicates that the entry
        name  (or  the CSECT name if there is no entry name) is to
        be used.
 
 
 NOTES:
 
    1.  The base register is BASER (see OSSETUP).
 
    2.  If SAVE=area is not specified, then no new save area  will
        be established.
 
    3.  The generated code does not depend on  register  15  being
        loaded    with    the    entry    point   address   unless
        ID=identification is specified.
1                           - 63 -
 
                 OSEXIT - Generate OS return code
+                ________________________________
 
 
 The OSEXIT macro will generate proper OS exit linkage code.
 
 <symbol> OSEXIT <(reg1,reg2)...>,<,SAVE=area><,LTR=reg>
                 <,PACK=YES><,RC=value><,FLAG=YES>
 
 
     reg1,reg2            registers
 
        Registers to be restored in  LM  format.   Any  number  of
        parenthesized  pairs  may  be specified.  When reg2 is the
        same as reg1, reg2 and the parentheses may be omitted.
 
     SAVE=area            relexpri
 
        The address of the program's register save area.
 
     LTR=reg              reg
 
        Requests that an LTR  reg,reg  be  performed  to  set  the
        condition code upon return.
 
     PACK=YES
 
        Must  be  specified  if  PACK=YES   was   coded   on   the
        corresponding OSENTER macro.
 
     RC=value             valuela
 
        Specifies a return code to be loaded into register 15.
 
     FLAG=YES
 
        Specifies that X'FF' is to be placed into  the  high-order
        byte  of  word  4 of the save area after the registers are
        restored.
 
 
 NOTE:
 
     If  SAVE=area  is  not  specified,  then  the  registers  are
     restored from the area pointed to by register 13.  Note  that
     SAVE=0(SAVER) and SAVE=0(13) are perfectly acceptable.
1                           - 64 -
 
             OSSETUP - Set up OS linkage environment
+            _______________________________________
 
 
 The OSSETUP macro, used once at the start of the  program  (after
 macro definitions, but before any code or EQUs), defines register
 names and optionally defines certain OS control blocks.
 
 symbol OSSETUP <REGS=option><,DCB=YES>
                <,R15=name><,R14=name><,R13=name><,BASER=name>
                <,R1=name><,R0=name>
 
 
     symbol                1-8 characters (required)
 
         CSECT name for the module.
 
     REGS=option           PLI or NO
 
         PLI is used to request PL/I compatible register
         definitions.  NO specifies that register definitions
         should not be included.
 
     DCB=YES
 
         Define OS DCB DSECT.
 
     R15=name               symbol
 
        Name to be used by OSENTER, OSEXIT and OSCALL to refer  to
        register 15.  Default is RCR.
 
     R14=name               symbol
 
        Name to be used by OSENTER, OSEXIT and OSCALL to refer  to
        register 14.  Default is RTNR.
 
     R13=name               symbol
 
        Name to be used by OSENTER, OSEXIT and OSCALL to refer  to
        register 13.  Default is SAVER.
 
     BASER=name             symbol
 
        Register to be loaded  by  OSENTER  as  a  base  register.
        Default is BASER.
 
     R1=name
 
        Name to be used by OSENTER, OSEXIT and OSCALL to refer  to
        register 1.  Default is VR1.
 
     R0=name
 
        Name to be used by OSENTER, OSEXIT and OSCALL to refer  to
        register 0.  Default is VR0.
1                           - 65 -
 
 
 
 NOTE:
 
     Register definitions are as follows:
 
                                Default         PLI
     Register   Absolute name   Symbolic name   Symbolic name
 
        0          R0               VR0           VR0
        1          R1               VR1           VR1
        2          R2               XRA, LOWR     XRA,HIGHR
        3          R3               XRB           XRB
        4          R4               XRC           XRC
        5          R5               XRD           XRD
        6          R6               XRE           XRE
        7          R7               XRF           XRF
        8          R8               XRG           XRG
        9          R9               XRH           XRH
       10          R10              XRI           XRI
       11          R11              XRJ           BASER,HIGHR
       12          R12              BASER, HIGHR  GCBR
       13          R13              SAVER         SAVER
       14          R14              RTNR          RTNR
       15          R15              RCR           RCR
 
     LOWR and HIGHR are for  use  with  OSENTER  and  OSEXIT  when
     specifying registers to be saved and restored.
1                           - 66 -
 
                OPENP - Check for successful open
+               _________________________________
 
 
 The OPENP macro will check DCBOFLGS to see if the DCB was  opened
 successfully.
 
 <symbol> OPENP dcb-addr
 
 
     dcb-addr             relexpri
 
         The address of the DCB to be checked.
 
 
 RETURNS:
 
     If the DCB was opened successfully, the condition  code  will
     be set to a non-zero value.
 
 
 NOTE:
 
     The DCBD macro must be included in the assembly.
1                           - 67 -
 
         CBDELINK - Remove control block from linked list
+        ________________________________________________
 
 
 CBDELINK is used to remove a control block from a linked list  of
 similar control blocks.
 
 <symbol> CBDELINK prev-reg,del-reg,work-reg,HEAD=loc
                   <,TAIL=loc>,NEXT=dsect-loc
                   <,BACK=dsect-loc>
                   <,CB=dsect-name><,ZOT=YES>
 
 
     prev-reg             preg
 
        Register must contain a pointer to the control block which
        immediately  preceeds  the  one  to  be  removed.   Should
        contain zero if removing from the beginning of the list.
 
     del-reg              preg
 
        Register must contain a pointer to the control block to be
        removed from the list.
 
     work-reg             preg
 
         A work register.
 
     HEAD=loc             relexpri
 
        Location of a word which contains a pointer to  the  first
        element  in  the  list.   Contains  zero  when the list is
        empty.
 
     TAIL=loc             relexpri
 
        Location of a word which contains a pointer  to  the  last
        element  in  the  list.   Contains  zero  when the list is
        empty.
 
     NEXT=dsect-loc       symbol
 
        Name of the word defined in a DSECT for the control  block
        which  points  to  the  next  control  block  in the list.
        Contains zero for the last element in the list.
 
     BACK=dsect-loc       symbol
 
        If present, indicates a doubly-linked  list  (forward  and
        backward  pointers).   Name of the word defined in a DSECT
        for the control  block  which  points  to  the  preceeding
        control  block  in  the list.  Contains zero for the first
        element in the list.
1                           - 68 -
 
 
 
     CB=dsect-id          symbol
 
        The name of the DSECT for the control block.  Omit if  the
        control block is defined with EQUs instead of a DSECT.
 
     ZOT=YES
 
        Indicates that the NEXT and BACK  fields  in  the  control
        block being removed should be set to zero.
1                           - 69 -
 
     CBDLINKH - Remove control block from head of linked list
+    ________________________________________________________
 
 
 CBDLINKH is used to remove the first control block from a  linked
 list of similar control blocks.
 
 <symbol> CBDLINKH del-reg,work-reg,HEAD=loc<,TAIL=loc>
                   NEXT=dsect-loc<,BACK=dsect-loc>
                   <,CB=dsect-name><,ZOT=YES>
 
 
     del-reg              preg
 
        Register must contain a pointer to the first control block
        in the linked list.
 
     work-reg             preg
 
         A work register.
 
     HEAD=loc             relexpri
 
        Location of a word which contains a pointer to  the  first
        element  in  the  list.   Contains  zero  when the list is
        empty.
 
     TAIL=loc             relexpri
 
        Location of a word which contains a pointer  to  the  last
        element  in  the  list.   Contains  zero  when the list is
        empty.
 
     NEXT=dsect-loc       symbol
 
        Name of the word defined in a DSECT for the control  block
        which  points  to  the  next  control  block  in the list.
        Contains zero for the last element in the list.
 
     BACK=dsect-loc       symbol
 
        If present, indicates a doubly-linked  list  (forward  and
        backward  pointers).   Name of the word defined in a DSECT
        for the control  block  which  points  to  the  preceeding
        control  block  in  the list.  Contains zero for the first
        element in the list.
 
     CB=dsect-id          symbol
 
        The name of the DSECT for the control block.  Omit if  the
        control block is defined with EQUs instead of a DSECT.
 
     ZOT=YES
 
        Indicates that the NEXT and BACK  fields  in  the  control
        block being removed should be set to zero.
1                           - 70 -
 
    CBDLINKT - Remove control block from tail of a linked list
+   __________________________________________________________
 
 
 CBDLINKT is used to remove the last control block from  a  linked
 list of similar control blocks.
 
 <symbol> CBDLINKT prev-reg<,del-reg>,work-reg,head=loc
                   <,TAIL=loc>,NEXT=dsect-loc
                   <,BACK=dsect-loc><,CB=dsect-name>
                   <,ZOT=YES>
 
 
     prev-reg             preg
 
        Register must contain a pointer to the control block which
        immediately  preceeds  the  one  to  be  removed.   Should
        contain zero if removing from the beginning of the list.
 
     del-reg              preg
 
        Register must contain a pointer to the control block to be
        removed from  the  list.   Required  only  if  ZOT=YES  is
        specified.
 
     work-reg             preg
 
         A work register.
 
     HEAD=loc             relexpri
 
        Location of a word which contains a pointer to  the  first
        element  in  the  list.   Contains  zero  when the list is
        empty.
 
     TAIL=loc             relexpri
 
        Location of a word which contains a pointer  to  the  last
        element  in  the  list.   Contains  zero  when the list is
        empty.
 
     NEXT=dsect-loc       symbol
 
        Name of the word defined in a DSECT for the control  block
        which  points  to  the  next  control  block  in the list.
        Contains zero for the last element in the list.
 
     BACK=dsect-loc       symbol
 
        If present, indicates a doubly-linked  list  (forward  and
        backward  pointers).   Name of the word defined in a DSECT
        for the control  block  which  points  to  the  preceeding
        control  block  in  the list.  Contains zero for the first
        element in the list.
1                           - 71 -
 
 
 
     CB=dsect-id          symbol
 
        The name of the DSECT for the control block.  Omit if  the
        control block is defined with EQUs instead of a DSECT.
 
     ZOT=YES
 
        Indicates that the NEXT and BACK  fields  in  the  control
        block being removed should be set to zero.
1                           - 72 -
 
            CBLINK - Add control block to linked list
+           _________________________________________
 
 CBLINK is used to add a control block anywhere in a  linked  list
 of similar control blocks.
 
 <symbol> CBLINK after-reg,new-reg,work-reg,HEAD=loc
                 <,TAIL=loc>,NEXT=dsect-loc,
                 <,BACK=dsect-loc><,CB=dsect-id>
 
 
     after-reg            preg
 
        Register containing a pointer to the control  block  after
        which  the  new  control  block  is  to  be added.  Should
        contain zero if the new control block is to  be  first  in
        the list.
 
     new-reg              preg
 
        Register must contain a pointer to the control block to be
        added.
 
     work-reg             preg
 
         A work register.
 
     HEAD=loc             relexpri
 
        Location of a word which contains a pointer to  the  first
        element  in  the  list.   Contains  zero  when the list is
        empty.
 
     TAIL=loc             relexpri
 
        Location of a word which contains a pointer  to  the  last
        element  in  the  list.   Contains  zero  when the list is
        empty.
 
     NEXT=dsect-loc       symbol
 
        Name of the word defined in a DSECT for the control  block
        which  points  to  the  next  control  block  in the list.
        Contains zero for the last element in the list.
 
     BACK=dsect-loc       symbol
 
        If present, indicates a doubly-linked  list  (forward  and
        backward  pointers).   Name of the word defined in a DSECT
        for the control  block  which  points  to  the  preceeding
        control  block  in  the list.  Contains zero for the first
        element in the list.
 
     CB=dsect-id          symbol
 
        The name of the DSECT for the control block.  Omit if  the
        control block is defined with EQUs instead of a DSECT.
1                           - 73 -
 
    CBLINKH - Add a control block at the head of a linked list
+   __________________________________________________________
 
 
 CBLINKH is used to add a control block at the start of  a  linked
 list of similar control blocks.
 
 <symbol> CBLINKH new-reg,work-reg,HEAD=loc<,TAIL=loc>,
                  NEXT=dsect-loc<,BACK=dsect-loc>
                  <,CB=dsect-id>
 
 
     new-reg              preg
 
        Register must contain a pointer to the control block to be
        added.
 
     work-reg             preg
 
         A work register.
 
     HEAD=loc             relexpri
 
        Location of a word which contains a pointer to  the  first
        element  in  the  list.   Contains  zero  when the list is
        empty.
 
     TAIL=loc             relexpri
 
        Location of a word which contains a pointer  to  the  last
        element  in  the  list.   Contains  zero  when the list is
        empty.
 
     NEXT=dsect-loc       symbol
 
        Name of the word defined in a DSECT for the control  block
        which  points to the next control block which in the list.
        Contains zero for the last element in the list.
 
     BACK=dsect-loc       symbol
 
        If present, indicates a doubly-linked  list  (forward  and
        backward  pointers).   Name of the word defined in a DSECT
        for the control  block  which  points  to  the  preceeding
        control  block  in  the list.  Contains zero for the first
        element in the list.
 
     CB=dsect-id          symbol
 
        The name of the DSECT for the control block.  Omit if  the
        control block is defined with EQUs instead of a DSECT.
1                           - 74 -
 
     CBLINKT - Add control block at the tail of a linked list
+    ________________________________________________________
 
 
 CBLINKT is used to add a control block at the  end  of  a  linked
 list of similar control blocks.
 
 <symbol> CBLINKT new-reg,work-reg,HEAD=loc,TAIL=loc,
                  NEXT=dsect-loc<,BACK=dsect-loc>
                  <,CB=dsect-id>
 
 
     new-reg              preg
 
        Register must contain a pointer to the control block to be
        added.
 
     work-reg             preg
 
         A work register.
 
     HEAD=loc             relexpri
 
        Location of a word which contains a pointer to  the  first
        element  in  the  list.   Contains  zero  when the list is
        empty.
 
     TAIL=loc             relexpri
 
        Location of a word which contains a pointer  to  the  last
        element in the list Contains zero when the list is empty.
 
     NEXT=dsect-loc       symbol
 
        Name of the word defined in a DSECT for the control  block
        which  points  to  the  next  control  block  in the list.
        Contains zero for the last element in the list.
 
 
     BACK=dsect-loc       symbol
 
        If present, indicates a doubly-linked  list  (forward  and
        backward  pointers).   Name of the word defined in a DSECT
        for the control  block  which  points  to  the  preceeding
        control  block  in  the list.  Contains zero for the first
        element in the list.
 
     CB=dsect-id          symbol
 
        The name of the DSECT for the control block.  Omit if  the
        control block is defined with EQUs instead of a DSECT.
1                           - 75 -
 
                       IX. ALP CODING HINTS
 
 
 1.  Use indentation to  indicate  the  nesting  level.   The  ALP
     listing  shows  the current nesting level to the left of each
     input line.  It is increased by BEGIN, <, CASE,  SELECT,  ASM
     CASE, ASM SELECT and MACRO and is reduced by END, >, ENDCASE,
     ENDSEL  and  MEND.   With  WYLBUR,  tabs can be set every few
     positions (say 3) and each line indented  by  the  number  of
     tabs equal to its nesting level.
 
 2.  Avoid using explicit branching or "GOTOs".  The  ALP  control
     structures show intent much more clearly.
 
 3.  Use the readability and environment macros  --  they make the
     intent of a program much clearer.
 
 4.  Use the assembler USING statement for "global" base registers
     and the ALP USE statement for "local" base registers.
 
 5.  Using symbolic register  names  makes  a  program  easier  to
     understand.   Name  registers  according  to  function.   The
     OSSETUP macro provides one possible set of names.
 
 6.  Never use two names for the same register in a single section
     of code.
 
 7.  Always use RGOTO instead of BR and GOTO instead of B (if  you
     must use explicit branching).
1                           - 76 -
 
                       X.  SAMPLE PROGRAM
 
 
 The following problem is taken from an actual class for beginning
 assembly language programmers.
 
 Given:  50 full words in  core,  each  containing  a  fixed-point
         (binary)  value.   The instructor will give you this data
         (in the form of DC statements) and describe the necessary
         JCL.  The first constant will be labeled NUMBERS.
 
 Task:   You are to determine the number  of  positive  constants,
         the  number  of negative constants and the number of zero
         constants, as well as the sum of each  of  these.   Store
         the  five computed values into core and output them via a
         core dump.  JFDUMP will be described in class.  Computing
         the sums will not result in overflow.
1                           - 77 -
 
 Assembly Language Solution:
 
 //  EXEC  ASMHCOMP
 //COMP.SYSIN  DD  *
 PROB1    START 0
          SAVE  (14,12),,*
          BALR  10,0
          USING *,10
          LA    12,SAVE
          ST    13,4(12)
          ST    12,8(13)
          LR    13,12
          LA    2,50                MAX TIMES THRU
          SR    3,3                 ZERO INDEX REG
          SR    4,4                 # OF POS VALUES
          SR    5,5                 # OF NEG VALUES
          SR    6,6                 # OF ZERO VALUES
 TOP      L     7,NUMBERS(3)        GET VALUE
          LTR   7,7                 SET CC
          BP    POS                 POSITIVE
          BM    NEG                 NEGAGIVE
          LA    6,1(,6)             BUMP ZERO CTR
 GOBACK   LA    3,4(,3)             BUMP POINTER
          BCT   2,TOP               KEEP GOING
          STM   4,6,NUMS            SAVE RESULTS
          JFDUMP START=PROB1,END=NUMS+12
          L     13,4(13)            GO BACK
          RETURN (14,12),RC=0
 POS      LA    4,1(,4)             BUMP COUNTER
          L     8,POSNUM            GET  # OF POS
          AR    8,7                 ADD TO IT
          ST    8,POSNUM            SAVE IT BACK
          B     GOBACK              KEEP GOING
 NEG      LA    5,1(,5)             BUMP COUNTER
          L     8,NEGNUM            GET NUMBER
          AR    8,7                 ADD TO IT
          ST    8,NEGNUM            RESTORE IT
          B     GOBACK              KEEP GOING
 SAVE     DC    18F'0'              SAVE AREA
 NUMBERS DC 2F'8,1,1,0,2,-2,0,3,-3,0,4,-4,0,5,-5,0,6,-6,0,7,-7,0,8,-8,0'
 POSNUM   DC    F'0'                POSITIVE VALUE
 NEGNUM   DC    F'0'                NEGATIVE VALUE
 NUMS     DS    3F                  COUNTERS
          END
 //  EXEC  ASMHLKGO
 //GO.SYSUDUMP DD SYSOUT=A
1                           - 78 -
 
 ALP Solution (without macros):
 
 //  EXEC  ALPHCOMP
 //COMP.SYSIN  DD  *
 PROB1: START 0;
 SAVE (14,12),,*;
 BALR 10,0; USING *,10;
 LA 12,SAVE; ST 13,4(,12); ST 12,8(,13);
 LR 13,12;
 
 LI 2,50;  % NUMBER OF TIMES THRU
 SR 3,3;  % CLEAR INDEX REGISTER
 SR 4,4;  % NUMBER OF POS VALUES
 SR 5,5;  % NUMBER OF NEG VALUES
 SR 6,6;  % NUMBER OF ZERO VALUES
 DO BEGIN
    L 7,NUMBERS(3);  % GET VALUE
    IF <LTR 7,7; CC Z> THEN LA 6,1(,6)  % ZERO VALUE
    ELSE IF <CC P> THEN BEGIN  % POSITIVE VALUE
       LA 4,1(,4);  % BUMP COUNTER
       L 8,POSNUM; AR 8,7; ST 8,POSNUM;  % COMPUTE SUM
       END
    ELSE BEGIN  % NEGATIVE VALUE
       LA 5,1(,5);  % BUMP COUNTER
       L 8,NEGNUM; AR 8,7; ST 8,NEGNUM;  % COMPUTE SUM
       END;
    LA 3,4(,3);  % BUMP POINTER
    END FOR 2;
 
 STM 4,6,NUMS;  % SAVE RESULTS
 JFDUMP START=PROB1,END=NUMS+12;
 L 13,4(,13);
 RETURN (14,12),RC=0;
 
 SAVE: DC 18F'0';  % SAVE AREA
 NUMBERS: DC 2F'8,1,1,0,2,-2,0,3,-3,0,4,-4,0,5,-5,0,6,-6,'_
               '0,7,-7,0,8,-8,0';
 POSNUM: DC F'0';  % POSITIVE VALUE
 NEGNUM: DC F'0';  % NEGATIVE VALUE
 NUMS:   DS 3F;
 END;
 //  EXEC  ALPHLKGO
 //GO.SYSUDUMP  DD  SYSOUT=A
1                           - 79 -
 
 ALP Solution (with macros):
 
 //  EXEC  ALPHCOMP
 //COMP.SYSIN  DD  *
 PROB: TITLE 'CLASS PROBLEM 1';
 PROB1: OSSETUP;
 SUBTITLE 'MAIN PROGRAM';
 OSENTER (RTNR,HIGHR),SAVE=SAVE,FORWARD=YES;
 
 LI XRA,50;  % NUMBER OF TIMES THRU
 ZR XRB;  % CLEAR INDEX REGISTER
 ZR XRC;  % NUMBER OF POS VALUES
 ZR XRD;  % NUMBER OF NEG VALUES
 ZR XRE;  % NUMBER OF ZERO VALUES
 DO BEGIN
    L XRG,NUMBERS(XRB);  % GET NUMBER
    IF <RZ XRG> THEN AI XRE,1  % ZERO VALUE
    ELSE IF <CC P> THEN BEGIN  % POSITIVE VALUE
       AI XRC,1;  % BUMP COUNTER
       L XRH,POSNUM; AR XRH,XRG; ST XRH,POSNUM;  % COMPUTE SUM
       END
    ELSE BEGIN  % NEGATIVE VALUE
       AI XRD,1;  % BUMP COUNTER
       L XRH,NEGNUM; AR XRH,XRG; ST XRH,NEGNUM;  % COMPUTE SUM
       END;
    AI XRB,4;  % BUMP POINTER
    END FOR XRA;
 
 STM XRC,XRE,NUMS;  % SAVE RESULTS
 JFDUMP START=PROB1,END=NUMS+12;
 OSEXIT (RTNR,HIGHR),RC=0,SAVE=SAVE;
 
 SUBTITLE 'CONSTANTS AND WORK AREA';
 SAVE: DC 18F'0';  % SAVE AREA
 NUMBERS: DC 2F'8,1,1,0,2,-2,0,3,-3,0,4,-4,0,5,-5,0,6,-6,'_
               '0,7,-7,0,8,-8,0';
 POSNUM: DC F'0';  % POSITIVE VALUE
 NEGNUM: DC F'0';  % NEGATIVE VALUE
 NUMS:   DS 3F;
 END;
 //  EXEC  ALPHLKGO
 //GO.SYSUDUMP  DD  SYSOUT=A
1                           - 80 -
 
                       XI. USING ALP AT NIH
 
 
 . The following procedures  are  available  and  conform  to  NIH
   conventions:
 
      ALP Procedure             Corresponding Assembler Procedure
+     _____________             _________________________________
 
 
        ALPHCOMP                          ASMHCOMP
        ALPHOBJ                           ASMHOBJ
        ALPHCOMF                          ASMHCOMP
        ALPHOBJF                          ASMHOBJ
        ALPHPRE                           None
        ALPHLKGO                          ASMHLKGO
        ALPHLDGO                          ASMHLDGO
        ALPHLKSM                          ASMHLKSM
        ALPHLKMM                          ASMHLKMM
        ALPHCALL                          ASMHCALL
        ALPHLOOK                          ASMHLOOK
 
   All symbolic parameters are the same.
 
 . Normally,  ALPHCOMP  and  ALPHOBJ produce only the ALP listing.
   However, if ASMLIST='' is specified on the EXEC statement,  the
   assembler listing will be produced as well.
 
 . ALPHCOMF and ALPHOBJF differ from ALPHCOMP and ALPHOBJ in  that
   the assembler listing is placed on microfiche.  Some additional
   symbolic parameters are provided to facilitate this:
 
      MFID=name                   Required.    Specifies   a   1-8
                                  character name  to  be  used  to
                                  insure  uniqueness of the DSNAME
                                  on the microfilm  tape.   Should
                                  begin with registered initials.
 
      MFNAME='dsname'             Optional.  Specifies the name of
                                  a  data  set  containing  PTFORM
                                  control   records.    A  default
                                  suitable for  most  applications
                                  is included.
 
      MFSTOR=unit                 Optional.  Specifies  unit  name
                                  for  the   PTFORM  control  data
                                  set.  Default is MFSTOR=FILE.
 
      MFDISK=volume               Optional.  Specifies the  volume
                                  on  which  the   PTFORM  control
                                  data set resides.
1                           - 81 -
 
 . The procedure ALPHPRE may be used to perform ALP  preprocessing
   without  assembling the result.  Normally, only the ALP listing
   is produced.  However, if ASMLIST=''  is   specified   on   the
   EXEC  statement  the  generated assembly code will be listed as
   well.
 
 . Problems or questions concerning ALP should be forwarded to the
   PAL Unit, Computer  Center,  DCRT,  Building  12A,  Room  1017,
   accompanied  by  a  PTR  (Programmer  Trouble  Report)  and all
   necessary computer runs.  This is currently the only method  of
   support for this product.
1                           - 82 -
 
                       XII. REFERENCES
 
 
 1.  Fletcher, J.  G.  et al., "On The  Appropriate  Language
 For  System  Programming",  SIGPLAN Notices Vol.  7, No.  7,
 (July 1972),28-32.
 
 2.  Lang, C.  A., "Languages for Writing  System  Programs",
 in   "Software   Engineering   Techniques".    NATO  Science
 Committee 101-106, April 1970.
 
 3.  Lyle, L.  M., "A Hierarchy of High Order  Languages  for
 Systems  Programming",  SIGPLAN  Notices  Vol.   6,  No.  9,
 (October 1971), 73&77.
 
 4.  Du Bois, P.  J.  et al., "The LRLTRAN Language  As  Used
 in  the  FROST  and  FLOE  Time-Sharing  Operating Systems",
 SIGPLAN Notices Vol.  6, No.  9, (October 1971), 92-104.
 
 5.  Haines, E.  C., "AL:  A Structured  Assembly  Language",
 M72-81,  The  MITRE Corp., Bedford, Mass., April 1972.  Also
 SIGPLAN Notices Vol.  8,  No.   1,  (January  1973),  15-20.
 Also SIGPLAN Notices Vol.  8, No.  4, (April 1973), 16-21.
 
 6.  Dijkstra, E.  W., "GO TO Statement Considered  Harmful",
 "Communications of the ACM", Vol.  11, No.  3, (March 1968),
 147-148.
1
                         COMMENT FORM
 
 Is the ALP User's Guide                       YES  NO
 
     Clear?                                    __   __
     Well Organized?                           __   __
     Complete?                                 __   __
     Accurate?                                 __   __
     Suitable for the beginner?                __   __
     Suitable for the advanced user?           __   __
 
 
 Comments:________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 _________________________________________________________________
 
 
 
 
 Please give page references where appropriate.   If  you  wish  a
 reply, include your name and mailing address.
 
 
                    Send to:  NIH
                              DCRT
                              Computer Center
                              Technical Information Office
                              Bldg. 12A, Rm. 1017
                              Bethesda, Maryland   20892
 ,SEPARATOR